## Slide 1: Performance of Shrinkage Estimators for Bioburden Density Calculations in Planetary Protection Probabilistic Risk Assessment
Andrei Griboka, Arman Seuylemezianb
a Idaho National Laboratory, Idaho Falls, ID, USA b Jet Propulsion Laboratory, California Institute of Technology, Pasadena, CA, USA
The Probabilistic Safety Assessment and Management conference (PSAM 16)
June 26-July 1, 2022
Honolulu, O’ahu, Hawaii USA
Jet Propulsion Laboratory
California Institute of Technology

## Slide 2: What Is Planetary Protection?
Mars
Forward Contamination
Backward Contamination
Why?
  How can we look for life on other planets if we bring our own?
  Meet NASA planetary protection requirements for launch approval.
  Comply with international treaty obligations.
Planetary protection (PP) aims to:
  Protect other worlds from microorganisms found on Earth.
  Prevent both forward and backward contamination.

## Slide 3: Bioburden Requirements for a Mars-bound and Outer Planets Biologically Sensitive Mission
PP requirements per NASA Procedural Requirements 8715.24:
For Mars:
  ≤5×105 total spores at launch
  ≤3×105 total spores on the planned landing hardware
  ≤300 spores/m2 on exposed surfaces.
For the outer planets:
  Inadvertent contamination of an ocean or other liquid water body is kept at a probability of less than 1 x 10-4 per mission.
Each biologically sensitive mission will develop a biological contamination control campaign that includes hardware design, material selection, material processing, manufacturing, assembly, testing, launch operations, space flight operations, and surface operations.
Microbial bioburden reduction and monitoring is conducted throughout the mission lifecycle.
Monitoring and/or verification of biological cleanliness is conducted using direct wipe and swab samples extracted and processed via a cultivation-based technique (NASA standard assay) that measures heat-tolerant organisms.
Notes: Primary driving factor for classification
1. Depends on the planetary body that its destined to (Mars, Europa, Enceladus)
2. Orbiter (trajectories)

## Slide 4: Planetary Protection Implementation Process Example
Clean
Determine the level of cleanliness
Keep it clean
e.g., protective cover, cleaning
Notes: Pictures from Mars Science Laboratory (Curiosity rover)
Image 1: Rover and Descent Stage
Image 2: Propulsion Tank
Image 3 : Heat Shield (Single Layer Insulation)
Image 4: Descent Stage
TSA plate – stock image

## Slide 5: Planetary Protection Biological Cleanliness Verification Sampling
Assay swab or wipe
(water is used as the solvent)
Count plates – 24 h, 48 h, and 72 h
Clean hardware (and table or bag) with an IPA wipe prior to sampling or installation
Process swabs and wipes,
~3 hours required post-assay
Notes: IPA – isopropyl alcohol
Image 1 (top left): descent stage telecom
Image 2 (top right): loop structures are for micrometerotie protection
Image 3 (bottom right): petri dishes
Image 4: spores

## Slide 6: Bioburden Accounting for Mars-landed Spacecraft Raw Spore Counts to Calculated Bioburden Levels
1970
2020
1990
2000
1980
2010
Mariner Mars
Viking Missions
Pathfinder
Mars Exploration Rovers
Mars Science Laboratory
InSight
Sum of the Means Approach
The total effective area sampled was represented by:
The total number of spores counted was:
The bioburden density, B, was given by:
B = Ntot / As
The estimate of the total bioburden, N, was given by:
N = B A0
Variable | Definition
A0 ns, nw ntot asi, awj fs, fw es, ew AS Nsi Nwj Ntot B | the total area represented by a group or sample set, m2 the total number of swabs or wipes the total number of samples is the area sampled by the ith swab and the jth wipe, (m2) the pour fractions for swabs and wipes the recovery efficiencies for swabs and wipes the total effective area, (m2) the number of CFU counted in the ith swab sample the number of CFU counted in the jth wipe sample the total number of CFU in a group, (spores/m2)
Poisson and Gaussian Statistics
Examples equations utilized:
NASA / Artist Illustration
NASA
NASA
NASA
NASA/JPL-Caltech/Lockheed Martin
NASA / Artist Illustration
Notes: Mariner mission orbiter
Viking- life detection mission
Pathfinder (table top size) are both landers
Mars Exploration Rover (two twin rovers) – golf cart size
MSL – mini cooper size
InSight – lander (this mission dataset is being used for Bayesian applications)
Sum of the means – 70s – 90s
Poisson and Gaussian – Pathfinder, MER and MSL

## Slide 7: Planetary Protection Dataset Overview – InSight Mission
Chart: # of Samples
| 41426 | 41456 | 41487 | 41518 | 41548 | 41579 | 41609 | 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221
Swabs | 39 | 0 | 12 | 0 | 0 | 0 | 0 | 0 | 16 | 12 | 17 | 56 | 55 | 68 | 32 | 84 | 129 | 94 | 63 | 79 | 115 | 56 | 17 | 8 | 15 | 18 | 41 | 0 | 39 | 46 | 6 | 213 | 0 | 42 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 7 | 22 | 17 | 50 | 74 | 57 | 25 | 10 | 0 | 0 | 52 | 194 | 42 | 53 | 48 | 0
Wipes | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 31 | 4 | 2 | 40 | 42 | 16 | 55 | 41 | 2 | 26 | 9 | 4 | 11 | 2 | 0 | 2 | 4 | 11 | 0 | 51 | 72 | 83 | 60 | 2 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 37 | 0 | 7 | 7 | 16 | 25 | 65 | 110 | 102 | 66 | 185 | 12
~10% of spacecraft surface areas were verified for biological cleanliness.
  2,031 swabs, 1,266 wipes, and 39,379 petri dishes were processed between June 2013 and May 2018.
  118,137 data points were recorded as part of the biological cleanliness verification campaign.
A majority of the samples yielded clean results.
  93% of the swabs and 63% of the wipes had 0 colony forming units (CFU), resulting in ~85% of the 39,379 petri dishes yielding 0 CFU (Hendrickson et al., Astrobiology 2019),
Notes: Swabs – 4 plates per swab
Wipes – 25 plates per wipe
Add axis label

## Slide 8: Summary of Bioburden Data for the Eight InSight Components
Component | CFU Count | Number of Samples | Area Sampled, m2 | Total Exposure: Area Sampled*Pour Fraction, m2 | Total Surface of the Component, m2 | % Sampled=Area Sampled/Total Area
9 | 0 | 49 | 0.6031 | 0.2167 | 0.7580 | 79.5650
38 | 12 | 27 | 3.1050 | 0.8065 | 10.0000 | 31.0500
67 | 0 | 27 | 2.4200 | 0.6160 | 2.7400 | 88.3212
169 | 1 | 17 | 0.2400 | 0.1920 | 0.5850 | 41.0260
243 | 5 | 34 | 0.2800 | 0.1140 | 0.2980 | 93.9600
261 | 52 | 24 | 0.0600 | 0.0480 | 0.3120 | 19.2310
283 | 5 | 8 | 4.5710 | 1.1427 | 12.0000 | 38.0920
300 | 1 | 9 | 2.6600 | 0.6705 | 5.0000 | 53.2000
Component 261 Sample # | CFUs observed | Area sampled, m2 | Pour fraction | Exposure, m2
1 | 1 | 0.0025 | 0.8 | 0.0020
2 | 0 | 0.0025 | 0.8 | 0.0020
3 | 0 | 0.0025 | 0.8 | 0.0020
4 | 0 | 0.0025 | 0.8 | 0.0020
5 | 0 | 0.0025 | 0.8 | 0.0020
6 | 0 | 0.0025 | 0.8 | 0.0020
7 | 0 | 0.0025 | 0.8 | 0.0020
8 | 0 | 0.0025 | 0.8 | 0.0020
9 | 0 | 0.0025 | 0.8 | 0.0020
10 | 0 | 0.0025 | 0.8 | 0.0020
11 | 0 | 0.0025 | 0.8 | 0.0020
12 | 0 | 0.0025 | 0.8 | 0.0020
13 | 3 | 0.0025 | 0.8 | 0.0020
14 | 0 | 0.0025 | 0.8 | 0.0020
15 | 0 | 0.0025 | 0.8 | 0.0020
16 | 0 | 0.0025 | 0.8 | 0.0020
17 | 0 | 0.0025 | 0.8 | 0.0020
18 | 0 | 0.0025 | 0.8 | 0.0020
19 | 0 | 0.0025 | 0.8 | 0.0020
20 | 6 | 0.0025 | 0.8 | 0.0020
21 | 8 | 0.0025 | 0.8 | 0.0020
22 | 10 | 0.0025 | 0.8 | 0.0020
23 | 10 | 0.0025 | 0.8 | 0.0020
24 | 14 | 0.0025 | 0.8 | 0.0020
Total | 52 | 0.0600 | 0.8 | 0.0480

## Slide 9: Data Poolability, Shrinkage Estimators, and Risk
Pooling is the process of grouping the data according to the values of bioburden density λ.
Data poolability can be statistically tested.
How can the data be grouped to minimize risk?
Shrinkage estimators perform partial pooling of the data and reduce risk.
Roughly only 10% of the spacecraft is sampled.
A constant estimator is an extreme example of a shrinkage estimator.
Constant estimators are used for both specified and implied components.
Shrinkage estimators are Bayesian estimators.
Risk is a measure of how far our estimate from the true and unknown values of bioburden density.
In the current work, the mean squared error (MSE) is assumed as a risk function.
B=0
B=1
B=1

## Slide 10: Zero Estimator for Gamma-Poisson Distribution Model
E
E

## Slide 11: Bias-Variance Decomposition-Posterior Mean Estimator (James-Stein), Borrowing Information
Notes: At 0.2, the estimator is using 80% of the information from the data and 20% from the prior
If e is large, we rely more on data. As e getting smaller, we need to rely more on prior.
B=0-no pooling of information, B=1-complete pooling of information.
There a range of B where EB-JS dominates MLE.

## Slide 12: Evaluating the Performance of Shrinkage Estimators
Poolable Data
From prior work, it was established that the bioburden density ranges from 1 CFU/m2 to 2,000 CFUs/m2.
To simulate poolable data, a vector of equally spaced λtrue was created.
Having fixed the exposure value (either swab or wipe) for each λtrue, 100 Poisson variables were generated.
Nine different estimators were applied to each generated sample of the Poisson variable.
For each estimator, the average MSE was calculated per:
The average MSE was plotted as a function of λtrue.
Non-poolable data
Since there is no single λtrue in this case, we treated the equally spaced vector of true λs as the vector of means of a gamma distribution with a variance of 105, which is approximately the variance of the population variability for bioburden data.
For each estimator, the average MSE was calculated per:
The average MSE was plotted as a function of λtrue, which is the mean of a gamma distribution.
Notes: The nine estimators were: MLE; zero estimator, which sets all estimates to zero regardless of the data; grand mean estimator, which pools all the data and is represented by Eq. 3; Empirical Bayes estimator, which uses the MOM to fit the prior distribution for λ; CZ estimator; Peng; modified Peng estimators; and two Tsui estimators, one shrinking to a prespecified mean value and the other shrinking towards the data median.

## Slide 13: Nine Estimators
9.
Notes: Clevenson-Zidek (CZ) shrinks towards zero, Peng shrinks towards zero and set samples with zero CFU counts to 0. Modified Peng shrinks towards zero , but does not set samples with zero CFU count to zero.
Tsui original estimator shrinks MLE towards predetermined value π. Tsui median estimator shrinks towards median value of the data

## Slide 14: Poolable Data
Swab Exposure, 0.002 m2
Wipe Exposure, 0.25 m2

## Slide 15: Non-poolable Data
Swab Exposure, 0.002 m2
Wipe Exposure, 0.25 m2

## Slide 16: Sample-to-Sample Variability of InSight Data
Sample-to-sample variability of InSight data, approximated by a gamma distribution with the following parameters: α = 0.0447, β = 2.5463∙10-4, λ average = 176 CFUs/m2, and λ variance = 7∙105 CFUs2/m4.

## Slide 17: Performance of Different Shrinkage Estimators on a Simulated Gamma Distribution of InSight Data
Swab Exposure, 0.002 m2
Wipe Exposure, 0.25 m2

## Slide 18: Conclusions
If the data are poolable, they must be pooled to reduce the risk.
For non-poolable data, different shrinkage estimators that perform superior to MLE can be applied to reduce the risk.
Different shrinkage estimators may perform better for different values of true λ.
An estimator is needed that will dominate others for practically meaningful values of true λ.
The performance of constant estimators is of significant importance, as these estimators represent the method implicitly applied to—and provide justification for using—specified and implied components.
If the accuracy of the spec values is known, it can be decided whether it is worth sampling a given component.
For the simulated InSight dataset, Tsui original estimator produces the lowest risk.