## Slide 1: Numerical Investigation of Flame Propagation for Explosion Risk Modeling Development
Ashley Coates1, Scott Lawrence1, Donovan Mathias1, Brian Cantwell2
1NASA Ames Research Center
2Stanford University, Aeronautics and Astronautics
PSAM 16 Conference
June 26 – July 1, 2022

## Slide 2: Motivation
Identify risk-driving failure mechanisms and help to evaluate overall design safety using probabilistic failure propagation and abort risk models
Gain understanding through high-fidelity simulations about the complex physics of flame propagation, debris strikes, overpressure, and other factors that could occur after an uncontained launch failure
Experiments
Engineering-level Blast Model
CFD Simulations

## Slide 3: Motivation
Many things can interfere with or change how the flame is propagating
Potential setup features considered in this work
Initial Pressure
Initial Velocity Distribution
Confinement
Obstacles
Multiple ignition points
Underlying flow conditions

## Slide 4: Problem Setup
Geometry representative of the Hydrogen Unconfined Combustion Test Apparatus (HUCTA) experiments conducted at MSFC
Experimental Setup
Computational Setup

## Slide 5: Problem Setup
Loci-Chem CFD Code
  Density-based, finite volume, unstructured solver
  2nd order accuracy time and space
  Navier-Stokes in three dimensions
  Viscous, turbulent, chemically reacting flows
Models
  Built-in database for transport and diffusion models
  Menter’s Baseline turbulence model
  7-species, 8-reaction H2-O2 chemistry model
Arrhenius Form k=ATBexp(-C/T)
Mesh
  Unstructured
  Grid spacing of 0.254 mm, order of laminar flame thickness
  Spacing very small in comparison to overall domain, use multiple meshes
  Assume axisymmetric, 2D mesh
Portion of mesh highlighting concentric regions

## Slide 6: Results and Discussion

## Slide 7: Quiescent Initial Pressure Variation
Stoichiometric
Hydrogen-Oxygen
Quiescent
Pinitial = 125 kPa
Temperature Contours [K]

## Slide 8: Compare to Experiment
Pressure varied in simulations, but at constant temperature, so density varied
Experimental data range determined from cases with approximately stoichiometric mixtures
x
Pressure not the driving factor for increased flame speed in experiment
More than 40% above ambient to reach experimental data range with quiescent simulation – not practical

## Slide 9: Initial Velocity Variation
Characterize potential effects an initial velocity distribution could have on the flame speed
Capture filling and recirculation processes observed in experiments
Velocity magnitude contours [m/s] of the three initial velocity distributions considered
Case 1: Shortest delay time, Highest initial velocity magnitude
Case 2: Middle delay time, Middle initial velocity magnitude
Case 3: Longest delay time, Lowest initial velocity magnitude
Case 1
Case 3
Case 2

## Slide 10: Initial Velocity Variation
Stoichiometric
Hydrogen-Oxygen
Middle Velocity Distribution, Case 2
Temperature Contours [K]

## Slide 11: Compare to Experiment
Reminder: Simulations did not model experiments exactly since experimental fill and recirculation process parameters were not reported and likely important
Presence and character of a non-uniform velocity field at ignition can significantly affect flame propagation behavior

## Slide 12: Engineering Model
Current engineering-level blast risk model used in support of NASA’s Space Launch System (SLS) program is analogous to the vapor cloud explosion model by Baker, Strehlow, and Tang
Solves one-dimensional Euler equations
Based on user-specified relative flame speed and level of heat addition, computed for multiple user-specified flame speeds to address uncertainties
Flame is tracked to the edge of a vapor cloud where a blast wave is initiated and propagated outward
Blast parameters are captured as a function of distance from the flame center

## Slide 13: Compare to Engineering Model
Pressure appears to be well resolved by the engineering model if the flame speed is known
Focus for furthering model capabilities should be placed on determining appropriate flame speeds

## Slide 14: Closing Remarks

## Slide 15: Conclusions and Future Work
Numerical simulations were computed for a variety of conditions and results were compared to experimental data and engineering model results. The gained understanding about influential parameters will lead to more informed flame speed numbers for risk assessments.
Conclusions
Setup procedures for both numerical and experimental studies can significantly affect flame speeds results – report information carefully
Flame speed is sensitive to initial conditions, particularly to interactions with underlying velocity flow features
Engineering model is well-suited to capture blast waves if the flame speed is known throughout propagation
CFD was useful for understanding and determining influential parameters
Future Work
Consider 3D effects
Determine how well flame speed needs to be captured to get good pressure results
Disseminate findings on local flame acceleration study

## Slide 16: References
[1] E. Richardson, T. Skinner, J. Blackwood, M. Hays, M. Bangham, and A. Jackson. “An experimental study of unconfined hydrogen/oxygen and hydrogen/air explosions”, 46th Joint Army- Navy-NASA-Air Force (JANNAF) Combustion Conference, (2014).
[2] Supercomputer Picture, https://images.nasa.gov/details-ARC-2008-ACD08-0272-002
[3] E. Luke and T. George. “Loci: A rule-based framework for parallel multidisciplinary simulation synthesis”, Journal of Functional Programming, 15, pp. 477–502, (2005).
[4] E. Luke. “On robust and accurate arbitrary polytope CFD solvers (invited)”, 18th AIAA Computational Fluid Dynamics Conference, (2007).
[5] E.A. Luke, X. Tong, J. Wu, P. Cinnella, and R. Chamberlain. “CHEM 3.3: A Finite-Rate Viscous Chemistry Solver - The User Guide”, (2014).
[6] Pointwise, Inc., https://www.pointwise.com/.
[7] Cantera, https://cantera.org.
[8] S.L. Lawrence and D.L. Mathias. “Blast overpressure modeling enhancements for application to risk-informed design of human space flight launch abort systems”, Reliability and Maintainability Symposium (RAMS), (2008).
[9] M.J. Tang and Q.A. Baker. “A new set of blast curves from vapor cloud explosion”, Process Safety Progress, 18, pp. 235–240, (1999).
Additional references in full paper

## Slide 17: Questions?
Thank You