## Slide 1: A Dynamic, Integrated Approach to Vital Area Identification
SAND2022-8717 C
Presented by:
Brian Cohn
Presented at The 16th Probabilistic Safety Assessment & Management Conference

## Slide 2: Introduction
The Design Evaluation Process Outline (DEPO) methodology is widely used for developing physical protection systems (PPSs)
Vital Area Identification (VAI) plays a key role in implementing the DEPO and other PPS design processes

## Slide 3: VAI Overview
VAI serves at the foundation for nuclear security analysis
  Based on static fault tree/event tree (FT/ET) analysis to determine vital equipment to protect with the physical protection system
  Vital areas are based on preventing severe core damage from adversary sabotage
Challenges with the VAI structure
  FTs are largely sourced from safety analysis with inbuilt safety assumptions that can be difficult to reevaluate
  VAI implies the instant onset of severe core damage following adversary sabotage of vital equipment
  For some scenarios, vital areas are only sabotage targets for a limited period of time
  Little communication between safety and security risks

## Slide 4: Previous Work
Integrated dynamic safety-security (2S) analysis of a hypothetical LWR
  Connected MELCOR reactor response analysis to security modeling
  Modeled successful sabotage of a complete target set
Case study found strong dynamic elements
  Level of damage from sabotage
  Success of mitigation and recovery actions
Minimal environmental releases

## Slide 5: Dynamic Approach to Vital Area Identification
Intent is to use 2S analysis to inform vital areas
  Identify adversary sabotage activities with associated timing
  Use timings to determine consequences to the reactor
Based on Systems Theoretic Process Analysis (STPA) and Dynamic Probabilistic Risk Assessment
  STPA is effective at systematically identifying systems of concern
    Poor at prioritizing between systems
  DPRA is effective at determining consequences of scenarios
    Poor at identifying scenarios of concern
Combined STPA and DPRA analysis can be more than the sum of its parts

## Slide 6: Proposed Dynamic VAI Approach
Initial Facility Design
SME/PRA/STPA for Target Sets
Dynamic Security
(e.g. PathTrace) Modeling
Design Basis Threat
SSC Targets
STPA Insecure Actions
Security Economic Model
Credible Adversary Scenarios
Time-Dependent Vital Areas
Identified Conservatisms within Static Analysis
Dynamic Linked Safety-Security
(Force-on-Force & Severe Accident)
Modeling
Final PPS for Facility Design
Safety Mitigations of Security Events
Areas to Reduce Conservatism
Re-evaluate PPS

## Slide 7: Phase 1
Purpose of this phase is to generate a comprehensive list of security-relevant systems
  Analysis is not concerned at this stage with the relationships between systems
  List of relevant systems can be obtained from:
    SME judgment
    PRA
    STPA
  Can include passive safety systems and digital controls

## Slide 8: Phase 2
Purpose of this phase is to generate conservative adversary attack timelines
  Dynamic security modeling used to understand the impact of sabotage
    PathTrace or other timeline model constructed
    Sabotage timings generated for each permutation of targets
    Timing information is sent to reactor response model to determine consequences of sabotage
    Output is a list of credible adversary scenarios
Reactor response strategies not considered in this phase

## Slide 9: Phase 3
Purpose of this phase is to determine the physical protection system’s effectiveness against the credible adversary scenarios
  Credible scenarios are entered into a force-on-force code
  Reactor response model receives information on damage to safety systems and determines appropriate responses
  Operator and response force activities can take the state of the plant into consideration
    Models mitigating actions
  Analysis can extend beyond core damage to radionuclide release
Similar to the previously described 2S analysis

## Slide 10: Proposed Case Study
A case study integrating all three phases has been proposed for analysis
  Uses the hypothetical Lone Pine Nuclear Power Plant
  Previously modeled during 2S analysis
Analysis is limited in scope to modeling the auxiliary feedwater (AFW) system
  Rest of the plant will be modeled, but only consider availability of AFW
Is intended to combine all three phases of the dynamic VAI approach
Considers the success of the reactor despite sabotage to vital equipment

## Slide 11: Conclusions
Existing VAI methodologies rely on conservatism to ensure the protection of NPPs
Limitations of static VAI present challenges for advanced reactors
  Reliance on passive safety systems
  Use of digital control systems
  Potential for adversaries to achieve some sabotage of systems
Proposed a dynamic VAI methodology
  STPA to systematically identify critical components
  DPRA to determine dynamic effects of adversary sabotage to components
Case study may be able to determine the effectiveness of the proposed methodology

## Slide 12: Questions?