## Slide 1: Capturing Epistemic Uncertainties in the Power Spectral Density for Limited Data Sets
Marco Behrendt1, Matthias G.R. Faes2,
Marcos A. Valdebenito3, Michael Beer1,4,5
1Institute for Risk and Reliability, Leibniz Universität Hannover, Germany
2Chair for Reliable Engineering, Technische Universität Dortmund, Germany
3Faculty of Engineering and Sciences, Universidad Adolfo Ibáñez,
Viña del Mar, Chile
4Institute for Risk and Uncertainty, University of Liverpool, United Kingdom
5International Joint Research Center for Engineering Reliability an Stochastic
Mechanics, Tongji University, Shanghai, China
PSAM 16 2022
Probabilistic Safety Assessment and
Management Conference
26 June – 1 July 2022
Honolulu, Hawaii

## Slide 2: Motivation
Buildings and structures are subject to environmental processes
  High-rise buildings
  Bridges
  Offshore-platforms
Hazards by environmental processes
  Earthquakes
  Wind loads
  Sea waves
Reliability of existing structures
Design safe structures
Dynamic behaviour
Time analyses and simulations

## Slide 3: Environmental processes
Environmental processes can be considered as stochastic processes
Power spectral density (PSD) function is widely adopted in modelling of stochastic processes
Interested in the influence of environmental processes to systems
  Apply data to a model with system excitation/response process

## Slide 4: Power spectral density estimation
Transformation from time domain to frequency domain
  Distribution of power into frequency components
  number of data points
  sampling time increment
  data point index
  integer frequency for

## Slide 5: Uncertainties in real data records
Real data records underlie uncertainties
Uncertainties must be quantified
  To ensure reliable simulation results
There is a need to represent the data in a manner suitable for application to systems
  A different form of the PSD function is derived from similar PSD functions

## Slide 6: Ensemble
PSD estimation

## Slide 7: Imprecise power spectrum
Identification of the basis power spectrum of the ensemble
Fitting an RBF network to the basis power spectrum
Adding/subtracting an interval parameter to/from each basis function to obtain a first approximation of the bounds
Optimisation of the interval parameter with minimum of constrained non-linear multi-variable function to obtain reliable bounds depending on the ensemble minimum and maximum

## Slide 8: Basis power spectrum
 midpoint spectrum mean spectrum

## Slide 9: Fitting an RBF network
RBF network Radial basis functions

## Slide 10: Optimisation of the bounds

## Slide 11: Sampling from the imprecise PSD
Determine reliability of structures by Monte Carlo simulation
Sampling uniformly distributed PSDs to generate time signals
  Spectral representation method is utilised
Tolerance factor ensures same energy content of sampled PSD
  No unrealistic PSD sampled (such as the upper bound)  does not reflect the stochastic process

## Slide 12: Numerical examples
Single-degree-of-freedom model:
Example 1)
  kg
  Ns/m
  N/m
Example 2)
  kg
  Ns/m
  N/m
For comparison: Mean value of an ensemble consisting of 100 PSDs

## Slide 13: Example 1

## Slide 14: Example 2

## Slide 15: Conclusion
Novel representation of the power spectral density function
  Set of discrete-valued power spectra is transformed to an interval-valued power spectrum
  Specifically useful for a limited amount of data is available
  Not possible to obtain reliable statistical information
Intervals instead of discrete values for each frequency
  Range of possible values identified by optimisation
  Does not rely on any distribution of the data within the bounds
Enables the quantification of uncertainties