## Slide 1: Epistemic Uncertainty Quantification of Localised Seismic Power Spectral Densities
Marius Bittnera,b, Marco Behrendta, Jasper Behrensdorfa, and Michael Beera,c,d
a Institute for Risk and Reliability, Leibniz Universität Hannover, Germany, bittner@irz.uni-hannover.de
b International Research Training Group 2657 - Computational Mechanics Techniques in High Dimensions, Ecole Normale Supérieure Paris-Saclay, France & Leibniz University Hannover, Germany
c Institute for Risk and Uncertainty, University of Liverpool, United Kingdom
d International Joint Research Center for Engineering Reliability and Stochastic
Mechanics, Tongji University, Shanghai, China
Probabilistic Safety Assessment and Management 16 June 26th - July 1st Honululu, Hawai’i

## Slide 2: Agenda
Motivation & Outlook
Theory & Details
Results & Conclusion

## Slide 3: Epistemic Uncertainty Quantification?
experiment
simulation
uncertain results of simulation
Seismic loads are considered epistemic input quantities
comparison
________________________________________________________________________________________________________________________ [1] Bai, Y., Li, Y., Tang, Z., Bittner, M., Broggi, M., Beer, M., 2021. Earthquake-induced collapse reliability of low-rise steel moment frames with additive-mass based on shaking table test. Bulletin of Earthquake Engineering
Notes: First of all, what exactly is meant with Epistemic uncertainty quantification? We want to increase the knowledge by refined model assumptions that are in the best case data driven. Mass on top is an additionall 2.25 tons First three storeys 42.5 tons last storey 38.5 tons

## Slide 4: Localised Seismic Power Spectral Densities
________________________________________________________________________________________________________________________ [2] Giardini, D. et al. (2003): The GSHAP Global Seismic Hazard Map. – In: International Handbook of Earthquake and Engineering Seismology, (International Geophysics Series, 81 B), Academic Press, 1233-1239.
Global Seismic Hazard Map [1]
How to perform accurate stochastic simulations for specific regions?
Notes: The colours from white to brown indicate a peak ground accelerations in from 0 to >4.8 m/s^2 with a 10% probability of exceedance in 50 years for a 475 years minimum time period. Mention source based ground acceleration method. (Strong motion Pulse Generation Areas)

## Slide 5: Large Database of information
________________________________________________________________________________________________________________________ [3] Luzi L., Lanzano G., Felicetta C., D‘Amico M. C., Russo E., Sgobba S., Pacor, F., & ORFEUS Working Group 5 (2020). Engineering Strong Motion Database (ESM) (Version 2.0). Istituto Nazionale di Geofisica e Vulcanologia (INGV). https://doi.org/10.13127/ESM.2
Notes: We may know the future location of our structure, however we may not know where the earthquake strikes exactly. Therefore measurements of the same earthquake can be assumed as possible inputs.

## Slide 6: Motivation: Find a generalized PSD description
Find a generalized stochastic model for the Power Spectral Density (PSD) function of specific localized events e.g. a specific earthquake.

## Slide 7: Simplified Problem
Sample function generation
Using stochastic methods does not lead to same signals
Fast Fourier Transform
Does not lead to the exact same PSD
[3]
[3]
[4]

## Slide 8
[3] M. Shinozuka, G. Deodatis, Simulation of Stochastic Processes by Spectral Representation, Applied Mechanics Reviews 44 (1991) 191–204, https://doi.org/10.1115/1.3119501.
[4] D. E. Newland, An Introduction to Random Vibrations, Spectral & Wavelet Analysis, Courier Corporation, 2012.

## Slide 9: Relaxed Power Spectrum estimation
________________________________________________________________________________________________________________________ [5] Behrendt, M. et al., (2022). Relaxed power spectrum estimation from multiple data records utilising subjective probabilities. Mechanical Systems and Signal Processing, 165
ensemble of PSDs
Relaxed Power Spectrum estimation
Using Truncated Normal Distributions

## Slide 10: Problems
In terms of the stochastic model with the TN-RPSD approach an increase of the random dimension is imminent.
Sections of the PSD function with a steep slope exhibit no accurately assigned probability density.
Sections of the PSD are defined as intervals with specific characteristics, the choice of the discretization of is therefore crucial for the representaiton.

## Slide 11: New approach – Sliced Normal Distributions
________________________________________________________________________________________________________________________ [6] L. G. Crespo, B. K. Colbert, S. P. Kenny, D. P. Giesy, On the quantification of aleatory and epistemic uncertainty using Sliced-Normal distributions, Systems & Control Letters 134 (2019) 104560, https://doi.org/10.1016/j.sysconle.2019.104560.
[7] B. K. Colbert, L. G. Crespo, M. M. Peet, A Convex Optimization Approach to Improving Suboptimal Hyperparameters of Sliced Normal Distributions, American Control Conference (ACC), 2020, pp. 4478–4483, https://doi.org/10.23919/ACC45564.2020.9147403.
Relaxed Power Spectral Density
Using Sliced Normal Distributions
A seamless multivariate PDF
Only 1 distriubtion to sample from
Correlation features are regarded

## Slide 12: Construction of Sliced Normal distributions (review)
Given data , number of available observations and dimension, construct a support set: , . A realization of is called (e.g. Monte Carlo Simulation) Define a mapping from physical space to a feature space
With
is suggested to contain a vector of monomials linked to the data and its dimension .

## Slide 13: Construction of sliced Normal distributions (review)
The Gaussian distribution for with mean value and the inverse of the covariance matrix is given to be
With respect to all previously defined hyperparameters and a suitable construction of the support set , following by scalable SN distribution is introduced

## Slide 14: Construction of Sliced Normal distributions (review)
can be solely determined by a data sequence Mean .
Via “Optimized Sliced Normals by Scaling the P Hyperparameter” [4] a new hyperparameter is introduced. With a numerical estimated in feature space [8] constant c can be approximated:
_________________________________________________________________________________________________ [8] M. J. Todd, Minimum-volume ellipsoids: Theory and algorithms, Society for Industrial and Applied Mathematics, 2016.

## Slide 15: Construction of Sliced Normal distributions (review)
On , with the representation of for the normalization constant c and the corresponding samples following statement is optimized towards ,
_________________________________________________________________________________________________ [9] J. A. Nelder, R. Mead, A Simplex Method for Function Minimization, The Computer Journal 7 (1965) 308–313, https://doi.org/10.1093/comjnl/7.4.308.
The hyperparameters are set, let‘s go.

## Slide 16
Notes: We have an issue here, the density is centered around the higher frequency parts. However we know that the PSD function is a continous function.

## Slide 17: Data-Thinning
First, the maximum and minimum values in for each frequency are captured by
next the difference of these vectors and is calculated to capture the magnitude of deviation, , from this difference, the maximum and minimum deviation is captured.
Notes: Therefore, a simple data-thinning algorithm is proposed, which is specifically tailored for functional data with similar characteristics.

## Slide 18: Data-Thinning
Given a linear interpolation function:
where define the rate how many samples shall be kept for the respected differences. To estimate the number of samples that can be deleted from the data for each discretized location following simple relation is given
for each discretized location in of the first samples are deleted. With this procedure each discretized value in is regarded as a single sample.

## Slide 20: Adaptive Sampling
Fin this example two dimensional samples can be generated by e.g. TMCMC. [10]
Let the sequence, ascendingly sorted by be denoted as . To ensure a conform reconstruction of single PSD functions, intervals are defined over the whole domain . For example, the cut-off frequency could be set as total upper boundary and the lower boundary.
________________________________________________________________________________________________________________________ [10] A. Gray, J. Behrensdorf, C. Scherrer, E. Miralles-Dolz, J. Storopoli, AnderGray/TransitionalMCMC.jl: v0.3.1, 2021, Zenodo, https://doi.org/10.5281/zenodo.4701274

## Slide 21: Adaptive Sampling
For each interval the first element in the sequence . is kept as final PSD function tuple. If no sample is falling in the predefined frequency subinterval, this subinterval is empty.
Formally this can be stated as

## Slide 22: PSD Modelling
= = 13

## Slide 24
Notes: Remember: we are modelling a Gaussian process.

## Slide 25
Figure 7: Averaged autocorrelation comparison for different sample sizes (10, 100, 500, 1000)

## Slide 26: Concluding Remarks
A Sliced Normals based formulation of a PSD ensemble has been proposed.
The accuracy of the shape (magnitude, coverage of areas) in comparison with the Truncated Normal RPSD representation is worse, however it seems that the features of the target stochastic processes are converging faster.
Optimality in Physical Space vs. Optimality in Feature Space [Crespo & Colbert]
For now only our toy example is regarded, this is highly unrealistic since the data-thinning and adaptive sampling only works because we actually know the shape of the true PSD.  A procedure for observation data only should be developed.
It is aimed to apply SN also for EPSD functions.
For Specific examples the Relaxed PSD can be directly transfomed into the response space.
Try other PSD driven stochastic process generators such as KL-Expansion.
Expand the applications also to wave, wind and other natural processes.

## Slide 27: Thank you very much for your attention!
Sliced Normals Framework:
https://github.com/FriesischScott/SlicedNormals.jl
Marius Bittner
bittner@irz.uni-hannover.de