## Slide 1
PSAM 2022
Issues and Approaches Regarding Success Terms for PRA Models
June 27 – July 1, 2022
James Knudsen

## Slide 2: PSAM 2022 – Success Term Process
Discussion Points
  Motivation of Success Term Process
  Objective of Success Term Process
  Current State-of-Practice Quantification
  Pros and Cons of the Current State-of-Practice
  Proposed Quantification Approach
  Pros and Cons of the Proposed Quantification Approach
  Results from Application of Success Term Process
  Conclusion

## Slide 3: PSAM 2022 – Success Term Process
Motivation of Success Term Process
  Complexity of Probabilistic Risk Assessment (PRA) models has increased over the past several years
    Internal event sequence quantification was understood to be slightly overestimated, but reasonable
      Majority of components random failure probabilities are small, i.e., <5.0E-2
    Inclusion of external events caused issues in sequence quantification
      Seismic PRAs
        Include high failure probabilities, i.e., >1.0E-1
        When possible, success probabilities are accounted for, creating non-coherent cut sets
      Fire PRAs
        Inclusion of spurious operation, human error probabilities, etc.

## Slide 4: PSAM 2022 – Success Term Process
Motivation of Success Term Process (cont.)
  Inclusion of external events along with internal events cause an overestimation of PRA frequency results
  This overestimation of the overall PRA frequency results can be substantial depending upon complexity of modeling
  This overestimation caused the research of different processes to sequence quantification

## Slide 5: PSAM 2022 – Success Term Process
Objective of Success Term Process
  Develop a process to properly account for high probability events in sequence quantification
    Reduce the overestimation of current state-of-practice quantification
    Eliminate work arounds to obtain reasonable overall results
      Force success events into sequence cut sets
      Gather cut sets into end states
  Be able to incorporate into existing analysis tools/approaches with minimal disruption

## Slide 6: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification
  Most PRA models use a linked fault tree approach
    Fault trees contain shared dependencies
    Accident sequences are mutually exclusive
    A simple summation of the sequences to obtain overall frequency
  Event tree (ET) nodes are usually binary and should sum to 1.0
  External event PRAs have high component failure probabilities, which defy the 1.0 binary split if not properly accounted
    This issue is the driver to the overestimation

## Slide 7: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification (cont.)
  Accident sequence cut sets are developed by creating two fault trees; failed fault tree and success fault tree
  Sequence 2 will be expanded for illustration

## Slide 8: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification (cont.)
  The failed and success fault trees for sequence 2 are

## Slide 9: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification (cont.)
  The failed and success fault trees shown on previous slide are solved to obtain minimal cut sets
  The failed cut sets are compared to the success cut sets
    Cut sets in the failed set are removed if they show up in the success set
    This is called “Delete Term” process
  Example:
  Failed Cut Sets Success Cut Sets
  BE-C * BE-F + BE-A +
  BE-B * BE-F + BE-C
  BE-D
  Cut set BE-C * BE-F in failed set will be removed based on the fact for the sequence to occur BE-C has to succeed

## Slide 10: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification (cont.)
  Given the process of accident sequence cut set generation, the current practice is to attempt to properly account for the success probability of ET nodes (top event fault trees)
    This approach can only be used if:
      Fault trees containing high probability components should only have 1 or 2 component basic events
      Fault trees are independent of the other fault trees within the ET accident sequence
    Cut sets are generated and quantified using minimal cut set upperbound approximation (Mincut) for each sequence
    Overall frequency result is then obtained by summing the result for all the accident sequences

## Slide 11: PSAM 2022 – Success Term Process
Current State-of-Practice Quantification (cont.)
  Often sequence cut sets are grouped into a single end state, reduced to just minimal cut sets for that group, and then quantified.
    This process typically results in a lower value since the success branch sequences do not explicitly include basic event success terms which can then result in few cut sets to be quantified.

## Slide 12: PSAM 2022 – Success Term Process
Pros and Cons of the Current State-of-Practice Quantification
  Pros
    Mincut approximation provides reasonable results given some independent high probability events are included
      Note: Binary Decision Diagram (BDD) quantification method provides a better estimate of the actual result than the mincut approximation
    Sensitivities studies are straightforward
    Level 2 analysis can be performed if cut sets are not gathered into an end state
  Cons
    Multiple complement basic events show up in cut sets, which can cause issues with Mincut approximation requiring BDD quantification
    Not being able to account for all high probability events due to complexity of fault trees and potential dependencies

## Slide 13: PSAM 2022 – Success Term Process
Proposed Quantification Approach
  Develop accident sequence specific success term recovery basic event to be applied to the sequence cut sets
  Two different methods to develop success term recovery basic event
    Method 1 – Use a “NOR” gate to generate success term cut sets and quantify those cut sets to obtain a success term value
    Method 2 – Use an “OR” gate to generate failure term cut sets, quantify those cut sets, and then subtract that value from 1.0 to obtain a success term value

## Slide 14: PSAM 2022 – Success Term Process
Proposed Quantification Approach (cont.)
  The success fault trees for both approaches
Method 1 NOR Gate
Method 2 OR Gate

## Slide 15: PSAM 2022 – Success Term Process
Proposed Quantification Approach (cont.)
  The success fault trees shown on the previous slide are solved to obtain minimal cut sets
    The cut sets from the NOR gate of Method 1 represent success, therefore this probability can be used directly for the sequence success term recovery event
    The cut sets from the OR gate of Method 2 represent failure, so this probability needs to be subtracted from 1.0 to be used as the sequence success term recovery event
Fault Trees | Cut Sets | MinCut | BDD | Sequence Success Term Recovery
Method 1 Success NOR | /BE-A * /BE-B * /BE-C + /BE-A * /BE-C * /BE-D * /BE-E | 5.01E-01 | 4.151E-01 | 5.007E-1 or 4.150E-1
Method 2 Success OR | BE-A + BE-C + BE-B * BE-E + BE‑B * BE-D | 5.941E-01 | 5.85E-01 | 1 - Pr(x) 1-5.94E-1 = 4.06E-1 1-5.85E-1 = 4.15E-1

## Slide 16: PSAM 2022 – Success Term Process
Proposed Quantification Approach (cont.)
  The quantified sequence specific success term recovery event is then ANDed to all cut sets within that sequence
    This process produces a more accurate result for each individual sequence than the current state-of-practice process
    All the success events, including complex ET nodes (fault trees) that have high probability events, are incorporated into final sequence cut sets
  This proposed quantification process provides a better estimate of the overall frequency since success terms that are typically ignored since they are assumed to be very close to a value of 1.0 are include in the quantification process

## Slide 17: PSAM 2022 – Success Term Process
Pros and Cons of Proposed Quantification Approach
  Pros
    Both methods calculate a better estimate of the overall frequency versus the current state-of-practice quantification since success events are factored into the results
    Method 2 is more straightforward in terms of quicker cut set generation and quantification
    Both methods allow for direct Level 2 evaluation and sensitivity studies
  Cons
    More quantification time than current-state-of-practice due to extra logic, cut set generation, and quantification to obtain sequence success term recovery event value to be applied to sequence cut sets
    Numerical round-off issues when probabilities are close to 1.0, i.e., 0.99999

## Slide 18: PSAM 2022 – Success Term Process
Results from Application of Success Term Process
  Success term process was applied to detailed seismic PRA
  The following is a generic seismic event tree that is used to solve 6 specific seismic bins
  Each seismic bin calculates a conditional probability of component failure and uses bin specific frequency

## Slide 19: PSAM 2022 – Success Term Process
Results from Application of Success Term Process (cont.)
  The table below compares results of the current state-of-practice versus the proposed Method 2 success term process
  The proposed success term process has results that are ~20% lower
Event Tree | Description | Current State of Practice |  | Proposed Process | 
Event Tree |  | MinCut | BDD | MinCut | BDD
EQK-BIN1 | Seismic Bin 1 (0.17g) | 1.13E-09/yr | 1.11E-09/yr | 1.12E-09/yr | 1.10E-09/yr
EQK-BIN2 | Seismic Bin 2 (0.39g) | 2.21E-07/yr | 2.12E-07/yr | 2.19E-07/yr | 2.09E-07/yr
EQK-BIN3 | Seismic Bin 3 (0.61g) | 2.29E-06/yr | 1.83E-06/yr | 2.23E-06/yr | 1.78E-06/yr
EQK-BIN4 | Seismic Bin 4 (0.87g) | 2.83E-06/yr | 1.71E-06/yr | 1.08E-06/yr | 5.86E-07/yr
EQK-BIN5 | Seismic Bin 5 (1.22g) | 2.34E-06/yr | 1.25E-06/yr | 2.32E-06/yr | 1.23E-06/yr
EQK-BIN6 | Seismic Bin 6 (2.12g) | 5.99E-07/yr | 2.28E-07/yr | 5.97E-07/yr | 2.28E-07/yr
Total |  | 8.28E-06/yr | 5.23E-06/yr | 6.44E-06/yr | 4.03E-06/yr

## Slide 20: PSAM 2022 – Success Term Process
Conclusion
  Issues with current state-of-practice quantification where success terms are not currently being addressed were presented
    Inability to account for high probability events due to ET node (fault tree) complexity
    Overestimation of results due to improper handing of ET node binary splits as success terms not explicitly included

## Slide 21: PSAM 2022 – Success Term Process
Conclusion (cont.)
  Two methods were proposed to better estimate individual sequence and overall frequency results
    Proposed sequence specific success term recovery better reflects logic and reduces overestimation of individual sequence and overall results
    Software modifications will be needed, but logic elements already exist
    High performance desktops and servers can minimize the additional time to more accurately quantify individual sequences and overall results

## Slide 22: PSAM 2022 – Success Term Process
    Questions