## Slide 1: Probabilistic Risk Assessment of the Molten Chloride Reactor Experiment Conceptual Design
Presented by
Jan Grobbelaar

## Slide 2: Acknowledgements
Co-Authors: Brian Johnson, Zander Mausolff, Jonathan Walker (Terrapower, LLC), Brandon Chisholm (Southern Company)
Reviewers: Troy Reiss, Jason Andrus (INL), Clint Medlock, Lauren Latham (Southern Company), Dan Walter (Terrapower LLC)
Southern Company
Idaho National Laboratory
National Reactor Innovation Center
ARDP Partners: Orano Federal Services, CorePower, Electric Power Research Institute
Department of Energy
This material is based upon work supported by the Department of Energy under Award Number DE-NE0009045.” Disclaimer: "This report was prepared as an account of work sponsored by an agency of the United States Government. Neither the United States Government nor any agency thereof, nor any of their employees, makes any warranty, express or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency thereof. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof

## Slide 3: MCRE Background
DOE awarded a contract to Southern Company-Services (SCS) Inc. for the design, development, and operation of the MCRE under the Advanced Reactor Demonstration Program.
SCS leads the project team including TerraPower, Idaho National Laboratory, Orano Federal Services, CorePower, 3M Company and the Electric Power Research Institute.
Mission Statement: To measure key reactor physics phenomena and test hypotheses about Molten Chloride Fast Reactor (MCFR) behavior, to reduce uncertainty and provide foundational knowledge to support the development of the MCFR Demonstration Reactor.

## Slide 4: MCRE Conceptual Design Features
Fast fission reactor (pool type)
Highly enriched NaCl-UCl3 eutectic fuel (1225 kg, HEU 630kg))
Low power (200 kW)
Very strong negative fuel density reactivity feedback coefficient
High fuel temperature (650 °C, ΔT = 10 °C)
Low pressure (100 kPa)
High fuel heat capacity => bulk freezing in ~40 hrs.
Passive decay heat removal
Functional containment

## Slide 5: MCRE Conceptual Design Systems
Reactor (1)
Pump (2)
Fuel salt drain tank (3)
Primary cooling fans (4)
Argon redundant supply tank (5)
Flush salt drain tank (6)
Fuel cask loading glove box (7)
Cover gas system delay tank (8)
Carbon beds (9)
Cooling coils (10)

## Slide 6: Licensing Modernization Project (LMP) Risk Informed Performance Based (RIPB) Approach (NEI 18-04)
Frequency-Consequence (F-C) targets
Safety Basis Events are to be plotted on this F-C targets as (dose, frequency) coordinates representing risk for comparison against dose limits
Defense-in-depth adequacy and accounting for uncertainty means that the F-C targets are not acceptance criteria
@NEI 2019, All rights reserved

## Slide 7: PRA Purpose
To risk-inform the selection of Safety Basis Events (a.k.a. Licensing Basis Events in NEI 18-04) to support the request for DOE approval of the MCRE conceptual design safety basis.
To risk-inform the safety classifications of the Systems, Structures and Components (SSCs).
To risk-inform design options or changes.
To develop institutional knowledge and experience in exercising the LMP RIPB process documented in NEI 18-04 to support the future MCFR-D licensing process

## Slide 8: PRA Development
DOE PRA Standard is not prescriptive
PRA development is to be in accordance with the ASME/ANS PRA Standard for Advanced Non-LWR Reactors
  Not all requirements applicable
The internal events PRA will be developed in accordance with following PRA elements: plant operating states, initiating events, event sequence analysis, success criteria, data analysis, system analysis, human reliability analysis, event sequence quantification, dose consequence analysis, and risk integration
External events PRA to be based on internal events PRA

## Slide 9: Plant Operation States

## Slide 10: Initiating Events
ART hazards analysis, ORNL MSRE unusual operating conditions, ORNL MSRE reactor safety analysis, a master logic diagram developed at TP, a recent MSR workshop publication.
  Decrease in fuel salt flow rate
  Increase in fuel salt flow rate
  Decrease in heat removal
  Increase in heat removal
  Reactivity and power distribution anomalies
  Fuel handling failures
  Leaks or ruptures
  Loss of offsite power

## Slide 11: Success Criteria
The fuel salt is maintained indefinitely inside the vessel in a non-critical liquid state by insertion of the control elements and applying the vessel heaters to add negative reactivity and prevent fuel freezing.
The fuel salt is off-loaded from the reactor vessel into the fuel salt drain tank which has a sub-critical geometry and decay heat can be indefinitely dissipated from the tank walls by convection to the LOTUS Testbed atmosphere.

## Slide 12: Data Analysis
With little operational and component reliability data available for MSRs, liquid sodium component reliability data have been used for salt-wetted components, as the pressure and temperature operating environments for salt and sodium are similar
  EGG-SSRE-8875, The Generic Component Failure Database for Light Water and Liquid Sodium Reactor PRA
Gas working fluid component data from
  WSRC-TR-S3-262, SAVANNAH RIVER SITE GENERIC DATA BASE DEVELOPMENT, Rev. 1”

## Slide 13: Accident Sequences
MCRE Transient Event Tree for POS-1 and POS-2

## Slide 14: DOE Frequency-Consequence Chart

## Slide 15: Conclusions
An internal events PRA has been developed to support the request for DOE approval of the MCRE Conceptual Design safety basis.
SBEs have been identified and plotted on DOE F-C targets, and preliminary results imply that safety class equipment would not be necessary from a RIPB point-of-view.
The PRA development will continue to evolve in parallel with subsequent design phases.

## Slide 16: Thank You! Questions?