## Slide 1: Synthesis of Questionnaire Insights Regarding Current PRA and Additional Tools
Joy Shen, Michelle T Bensi, and Mohammad Modarres
University of Maryland, College Park, MD, USA
jshen132@umd.edu; mbensi@umd.edu; modarres@umd.edu
This research is supported by the U.S. Nuclear Regulatory Commission. Any opinions, findings, and conclusions expressed in this paper/presentation are those of the authors and do not necessarily reflect the views of the funding agency or any other organization. The authors acknowledge and appreciate the valuable insights provided by subject matter experts who responded to the anonymous questionnaire discussed in this paper.
Notes: Joy Shen graduated with a B.S. in Mechanical engineering and an minor in Nuclear engineering from the University of Maryland at College Park. She stayed at Maryland and is currently a PhD candidate in the Reliability Engineering program, advised by Dr. Bensi and Dr. Modarres. Her research focuses on advanced PRA development, and PRA tool improvement, especially applied to external flooding hazards.

## Slide 2: Introduction
Event Tree and Fault Tree Analyses (ETA/FTA) are the foundational tools of the conventional PRA framework
The needs of the PRA community have evolved
Available technologies and tools have improved
Need to reassess available PRA tools and how they address the community needs and contribute to the risk informed decision making (RIDM) process

## Slide 3: Questionnaire
What static PRA software do you have experience using? Select multiple if applicable.
  SAPHIRE
  Riskman
  RiskSpectrum
  CAFTA
  WinNUPRA
  FRANX
  Other (Please Specify)
  I do not use PRA tools

## Slide 4: Questionnaire
2) What are the strengths of the PRA software/tools you are using/have used? If you discuss multiple tools, please connect each tool to its strengths.
3) What are the limitations of the PRA software/tools you are using/have used? If you discuss multiple tools, please connect each tool to its limitations.
4) What other tools or software have you used to supplement the PRA tools/software you identified above? Why have they been needed? If you discuss multiple tools, please connect each tool to its necessity.

## Slide 5: Questionnaire
5) What types of PRAs have you worked on when using the tools/software/methods identified above? (e.g., internal events, internal flooding, fire, seismic, high winds, external flooding, human risk assessment (HRA), data analysis, level II/III,...)
6) What types of nuclear power technologies do you work with when using the tools/software/methods identified above? (e.g., LWRs, SMRs, gas reactors, breeder reactors, molten salt reactors,...)
7) Please provide additional comments regarding the potential for new or existing PRA tools (used within or outside the nuclear industry) to meet the evolving needs of the nuclear industry.

## Slide 6: Questionnaire Characteristics
Sent to 431 members of the international PRA community
52 anonymous responses
  Gathered insights on:
    PRA tool experience
    Advantages/limitations
    PRA community needs
Work is ongoing and will continued to
be shared with the community
Scan above to share your insights

## Slide 7: Questionnaire Characteristics
Survey supplemented questionnaire to create comprehensive analysis.
Responses subject to opinion and personal beliefs
Questionnaire Response to Conventional PRA Tool Experience

## Slide 8: Questionnaire Responses on Conventional PRA Tools
Traditional PRA methods (Event Tree/Fault Tree analysis)
e.g. SAPHIRE, Riskman, Risk Spectrum, CAFTA, WinNUPRA
Ease of use
Software compatibility
Model
visualization/
navigation
Post-processing capabilities
Quantification efficiency /inefficiency
Comprehensive/
Limited external
hazard capabilities
Advantages
Limitations
Conflicting Insights

## Slide 9: Questionnaire Responses on Dynamic PRA Tools
Dynamic PRA methods
e.g. EMRALD, RAVEN, ADS-IDAC, CFAST, FRI3D, Crystal Ball
Ease of use
Software compatibility
Efficient quantification
High
computational
requirement
Complex model limitations
Comprehensive/
Limited risk
assessment
capabilities
Advantages
Limitations
Conflicting Insights

## Slide 10: Questionnaire Responses on Severe Accident/Thermohydraulic Tools
Accident progression or thermal-hydraulic behavior
e.g. RELAP, TRACE, SCDAP/RELAP5, MAAP, MELCOR, MACCS
Large user base
Enhances accident modeling
Further informs PRAs
High computational requirement
Modeling capabilities
Advantages
Limitations
Conflicting Insights

## Slide 11: Questionnaire Responses on Supplemental and Miscellaneous Tools
Provides additional information to the PRA
e.g. FTREX, PRAQuant, UNCERT, XFTA, ACUBE, SYSIMP, MSCAL, EVNTRE, FRANX, GOFACS, PHOENIX, EPRI HRA Calculator
Ease of use
Efficient quantification
Software compatibility
High computational requirement
User-interface
Model setup time
Risk assessment capabilities
Advantages
Limitations
Conflicting Insights

## Slide 12: Questionnaire Responses on Novel PRA tools
Expands traditional PRA scope
e.g. AIMS-PSA, Isograph, Phoenix Architect, PSAPACK, KANT, Andromeda, SCRAM, KB3
Ease of use
Software compatibility
Post-processing
User-interface
Risk assessment capabilities
Advantages
Limitations
Conflicting Insights

## Slide 13: Questionnaire Responses on General-Purpose Tools
Pre/post processing data
e.g. Excel, general programming codes, Open Bugs/WinBugs, CCFWin
Customizable data visualization
Organizes results
Integration into PRA software
Requires prior external knowledge
Advantages
Limitations
Conflicting Insights

## Slide 14: Questionnaire Responses on HRA Models:
Human behavior and reliability assessments
e.g. PANAME, HORAAM, SPAR-H Model
Well-established
Expands the PRA scope
Task representation
Limited guidance
Advantages
Limitations
Conflicting Insights

## Slide 15: Summary of Current Tool Advantages
User experience improvements potentially make it easier for more practitioners to enter the community
  User interface, training, user base
Improvements in algorithms, risk assessment functionalities, computational abilities to handle larger/complex models
Numerous tools expand the traditional PRA scope and methods

## Slide 16: Summary of Current Tool Limitations
PRA community is looking for increased interfacing and integration of analyses

## Slide 17: Summary of Inconsistencies about Current Tools
Inconsistencies in insights among respondents are subjected to the individual user’s opinion
  Quantification speed
  Model setup ease
  XHPRA functionality comprehensiveness
  Software integration

## Slide 18: PRA Community Needs
Traditional PRA Framework
Dynamic PRA
Post/Pre Processing Data
Supplemental Information
HRA
Collaboration

## Slide 19: PRA community needs
Integration/interfacing/development of…
  Dynamic PRA
    Believed to be the PRA community’s next focus
  Post/Pre-processing
    Standardizing data
    Information sharing to stakeholders or other practitioners
    Result presentation

## Slide 20: PRA community needs
Integration/interfacing/development of…
  Supplemental Information
    Physical models
    CCF
  Collaboration
    Facilitate information sharing and integrating interdisciplinary skills
    Model management
    Version control

## Slide 21: PRA community needs
Integration/interfacing/development of…
  HRA
    Expand PRA scope

## Slide 22: Conclusion
Community favors a hybrid combination of conventional, novel and additional PRA tools
Tools have enhanced in computational capabilities and functionalities
Questionnaire highlights the trends the PRA community are moving towards
  i.e., XHPRA, dynamic PRA, collaboration

## Slide 23
  Questions?
  Have something to add?
  Scan the QR code and share with us now!
This research is supported by the U.S. Nuclear Regulatory Commission. Any opinions, findings, and conclusions expressed in this paper/presentation are those of the authors and do not necessarily reflect the views of the funding agency or any other organization. The authors acknowledge and appreciate the valuable insights provided by subject matter experts who responded to the anonymous questionnaire discussed in this paper.

## Slide 24: References
[1] S. Kaplan and B. J. Garrick, “On The Quantitative Definition of Risk,” Risk Analysis, vol. 1, no. 1, pp. 11–27, 1981, doi: 10.1111/j.1539-6924.1981.tb01350.x.
[2] "Systems Analysis Programs for Hands-on Integrated Reliability Evaluations (SAPHIRE): Summary Manual." Accessed: Sep. 23, 2021. [Online]. Available: https://www.nrc.gov/reading-rm/doc-collections/nuregs/contract/cr6952/v1/index.html
[3] D. Wakefield, S. Epstein, Y. Xiong, and K. Nouri, "RISKMAN®, celebrating 20+ years of excellence!," 10th Int. Conf. Probabilistic Saf. Assess. Manag. 2010 PSAM 2010, vol. 4, pp. 3488–3497, Jan. 2010.
[4] S. Prescott, C. Smith, and L. Vang, "EMRALD, Dynamic PRA for the Traditional Modeler," Los Angel., p. 12, 2018.
[5] A. Alfonsi, D. Mandelli, C. Parisi, and C. Rabiti, "Risk analysis virtual ENvironment for dynamic event tree-based analyses," Ann. Nucl. Energy, vol. 165, p. 108754, Jan. 2022, doi: 10.1016/j.anucene.2021.108754.
[6] A. Alfonsi, C. Rabiti, D. P. Maljovec, D. Mandelli, and C. L. Smith, "Enhancements to the RAVEN code in FY16," INL/EXT--16-40094, 1369372, Sep. 2016. doi: 10.2172/1369372.
[7] A. Alfonsi, C. Rabiti, D. Mandelli, J. Cogliati, S. Sen, and C. Smith, "Improving Limit Surface Search Algorithms in RAVEN using Acceleration Schemes."
[8] "ADS-IDAC," The B. John Garrick Institute for the Risk Sciences. https://www.risksciences.ucla.edu/adsidac (accessed Mar. 04, 2022).
[9] M. A. Diaconeasa and A. Mosleh, "Performing an Accident Sequence Precursor Analysis with the ADS-IDAC," in Los Angeles, 2018, p. 7.
[10] "COMPUTER CODES FOR LEVEL 1 PROBABILISTIC SAFETY ASSESSMENT," p. 103.
[11] A. Prošek and M. Matkovič, "RELAP5/MOD3.3 Analysis of the Loss of External Power Event with Safety Injection Actuation," Sci. Technol. Nucl. Install., vol. 2018, p. e6964946, Apr. 2018, doi: 10.1155/2018/6964946.
[12] "Computer Codes," NRC Web. https://www.nrc.gov/about-nrc/regulatory/research/safetycodes.html (accessed Sep. 24, 2021).
[13] W. Tietsch, “RELAP5/MOD3.3 Release Pre & Postprocessor.” International Agreement Report.
[14] "Modular Accident Analysis Program (MAAP5) Version 5.02 - Windows." https://www.epri.com/research/products/1021648 (accessed Mar. 04, 2022).
[15] "Containment Modeling using MAAP."

## Slide 25: References
[16] J. L. LaChance et al., "Development and Application of a Dynamic Level 1 and 2 Probabilistic Safety Assessment Tool," p. 10.
[17] A. Hakobyan, "Severe Accident Analysis using Dynamic Accident Progression Event Trees," Ohio State University, 2006.
[18] K. Sunnevik, “Comparison of MAAP and MELCOR.” Uppsala Universitet.
[19] W. S. Jung, "FTREX Features for a Multi-Unit PSA," presented at the Transactions of the Korean Nuclear Society Spring Meeting, Jeju, Korea, May 2018. Accessed: Feb. 03, 2022. [Online]. Available: https://www.kns.org/files/pre_paper/39/18S-696%EC%A0%95%EC%9A%B0%EC%8B%9D.pdf
[20] M. Marcilhac, N. Rahni, E. Raimond, E. H. Moussi, K. Maccoco, and G. Blondet, "Gofacs: Generator Of Fragility Assessment For Coupled Systems, Structures And Components," Uncertain. Quantif., p. 8, 2021.
[21] S. H. Han, J.-E. Yang, and S.-C. Jang, "AIMS-PSA : A Software for Integrating Various Types of PSAs," p. 20.
[22] "Reliability Workbench," Isograph, Nov. 26, 2019. https://www.isograph.com/software/reliability-workbench/ (accessed Mar. 04, 2022).
[23] T. Friedlhuber, “Model Engineering in a Modular PSA,” p. 229.
[24] "WinBUGS," MRC Biostatistics Unit. https://www.mrc-bsu.cam.ac.uk/software/bugs/the-bugs-project-winbugs/ (accessed Mar. 07, 2022).
[25] E. Engineering, "NUREG-2127, 'The International HRA Empirical Study: Lessons Learned from Comparing HRA Methods Predictions to HAMMLAB Simulator Data'.," p. 157.
[26] V. Fauchille, "Application of the HORAAM method for the updating of the IRSN Level 2 PSA Model," presented at the PSAM 9.
[27] R. Boring and D. Gertman, "P-203: Human Reliability Analysis (HRA) Training Course," INL/EXT--17-40997-Rev000, 1467594, Mar. 2016. doi: 10.2172/1467594.
[28] D. I. Gertman, H. Blackman, J. Marble, J. Byers, and C. Smith, "The SPAR-H Human Reliability Analysis Method." USNRC, Aug. 2005