## Slide 1
Global Expertise • One Voice
Benefits and Lessons Learned from PRA / Operations Interface at Nuclear Power Plants
N. Reed LaBarge (Westinghouse / PWROG)
Jayne Ritter (Xcel Energy / PWROG)
Brad Dolan (TVA / PWROG)
Probabilistic Safety Assessment and Management PSAM 16
June 26th, 2022 – July 1st, 2022

## Slide 2
Topics
Introduction / Background
Enhancements to Generic Procedure Sets and HRA Methods
Enhancements to Plant-Specific Procedures and HRA
Summary, Contact Information and Q&A

## Slide 3
Introduction / Background

## Slide 4
PWROG PRA / Operations Interface
Risk Beneficial Procedure Change (RBPC) Core Team
  Formed in 2019
  Membership:
    13 PRA Experts
    13 Current or Formerly Licensed Nuclear Operators
    2 Safety Analysis Experts
  Accomplishments
    Monthly Core Team Meetings
    How to Proceduralize New Functions Using FLEX Equipment
    Best Practices for the Plant-Specific Operations / PRA Interface
    Workshops on Improving Realism in HRA

## Slide 5
Enhancements to Generic Procedure Sets and HRA Methods

## Slide 6
Generic Procedure Enhancements
PWROG Generic Procedure Sets Include:
  Emergency Operating Procedures (EOPs)
  FLEX Support Guidelines (FSGs)
  Select Abnormal Operating Procedures (AOPs)
Risk Beneficial Plant Functions with FLEX Strategies
  Low Pressure Auxiliary Feedwater (AFW) pumps
  AFW Suction Source (long term AFW for plants with small CST)
  Backup Electrical Power (AC & DC)
  Ultimate Heat Sink (UHS)
  Decay Heat Removal via Steam Generators (SGs)

## Slide 7
Generic HRA Insights and Best Practices
Treatment of repair / unavailability is likely conservative
  Availability of equipment can be different in different situations
  Cognitive Unrecovered Trees in HRA Calculator
  Indication Available in the Control Room
    As long as the control room can get the information you can select yes
  Control Room Indication Accurate
    For fire events, plants may have proceduralized guidance for how to confirm indications using a separate device – this can be credited in Fire HRA for example
  Low vs. High Workload
    This is subjective; utility operations teams should weigh in on guidance for how to answer questions related to workload

## Slide 8
Generic HRA Insights and Best Practices
  Cognitive Unrecovered Trees in HRA Calculator (cont.)
  Check vs monitor
    Monitoring may be more beneficial than is being credited, especially if this is a critical parameter that is central to the operation of the plant
  Front vs. Back panel
    This really doesn’t make a big difference for operators who are instructed to check parameters regardless of their location
  Graphically Distinct
    If it has a number / letter / designator it should be considered distinct
  Standard or Ambiguous Wording
    In modern PWROG member EOPs, this is essentially all considered to be standard wording

## Slide 9
Generic HRA Insights and Best Practices
  Notes and feedback on Execution Stress
  Plant Response as Expected
    Most standard actions should be interpreted as plant response as expected
  Dependency Analysis
  Generally, the team members with an operational background believe the dependent Human Error Probabilities (HEPs) that are being provided by THERP are conservative
  Intervening Success
    This may be a place where the industry should spend more time thinking about when this is applicable (i.e., it may be applicable more than we are typically giving it credit for).
  Common Cognitive
    Separating out the cognition and the execution portions of the operator action will remove the dependency for the execution

## Slide 10
Enhancements to Plant-Specific Procedures and HRA

## Slide 11
Best Practices for Plant-Specific Operations / PRA Interface
  Regular meetings between PRA leads and plant operations and training staff and are beneficial
  Feedback on HRA Methods
  Latest Operator Performance Timings
  Review Risk-Significant Operator Actions
  Minimum Frequency
  Changes to EOPs (or procedures referenced in HRA Notebook)
  New or upgraded PRA Hazard models
  Change in highest contributors to risk (accident sequences / operator actions / hazard models)

## Slide 12
Best Practices for Plant-Specific Procedure Updates
  Considerations for Adding Beyond Design Basis Strategies to Procedures
  Include how to restore the credited strategy when it becomes available or is ready to be returned to service
  Equipment may need to be pre-staged to ensure the FLEX action is viable
  Strategies for Improving Defense in Depth in Emergency Procedures
  FLEX can be used as long as the credited strategy is lost and other credited strategies are not interrupted
  Strategies for Replacing a Function lost due to Maintenance or Surveillance
  Inform plant staff regarding how to log the availability / unavailability
  Consider staging a piece of FLEX equipment for use if the redundant train fails unexpectedly

## Slide 13
Best Practices for Plant-Specific Procedure Updates (cont).
  Considerations for Procedure Changes to Improve Time Margin in Operator Actions
  Consider laminating a portion of a procedure and having it available in the control room (i.e., developing a “hard card”) for a combination of alarms
    Hard cards can be faster than going through a procedure
    Verbal communication can take time
    Provides more consistent margin on the time response
  Considerations for Plant-Specific Procedure Changes to Reduce Risk
  Add steps to locally start equipment to address equipment that failed to start from failure of the auto-start

## Slide 14
Summary, Contact Information and Q&A

## Slide 15
Summary
The PWROG has been focusing on generically improving the relationship between utility PRA group leads and utility procedure writers
RBPC established in 2019
  Half PRA Experts; Half Operators / Procedure Writers
  Best Practices, Operational Experience, Refining HRA Methods
  Communication Throughout Industry

## Slide 16
Contact Information
PWROG Management Contact Information

## Slide 17
Contact Information
Additional Author Contact Information

## Slide 18
Thank you for your Attention!
Questions?