## Slide 1
Gabriel San Martín Silva (gsanmartin@ucla.edu)
Tarannom Parhizkar (tparhizkar@ucla.edu)
Enrique López Droguett (eald@ucla.edu)
Quantum Fault Trees
Department of Civil & Environmental Engineering,
The B. John Garrick Institute for the Risk Sciences,
University of California, Los Angeles

## Slide 2: Introduction
Engineering systems have been growing in both size and complexity for decades
New challenge in PRA: scalability and efficiency when trying to solve increasingly challenging problems
A promising field to achieve speed up and memory efficiency is quantum computing
Early exploration of quantum computing applied to Fault Trees
We propose an encoding method to represent systems as quantum circuits

## Slide 3
Quantum Computing Basics

## Slide 4: Quantum Information
Basic unit of classical information: on-off
Same concept, but for a quantum system:
, with
  The basis states are obtained when or
The qubit allow us to represent quantum mechanics phenomena such as superposition, entanglement or interference

## Slide 5: Quantum Information Processing: Gates
Operations between one or more qubits are known as gates (similar to logic gates)
Mathematically, gates are represented by unitary matrices:
  Its conjugate transpose is also its inverse
  is a complex square matrix
  is the conjugate transpose referred to the Hermitian adjoint
  is the identity matrix
Thus, quantum gates are reversible

## Slide 6: Quantum Gates
Negation: NOT gate (or Pauli-X)

## Slide 7: Quantum Gates
Superposition: Hadamard gate

## Slide 8: Quantum Gates
Entanglement: C-NOT gate.
The C-NOT gate acts on a two-qubit system, generating a dependency relationship

## Slide 9: Rotation Gates: The Bloch Sphere
It is useful to represent a single qubit as a point in a unitary sphere (Bloch Sphere).
Naive representation: 4 parameters
It can be shown that these 4 parameters can be reduced to 2 free parameters [1]
This is useful for a fundamental set of gates: the rotation gates.

## Slide 10: Rotation Gates
The rotation gates generate a shift of angle in any of the three axis of the Bloch sphere:

## Slide 11
Quantum Representation of Logic Gates

## Slide 12: Quantum Circuits
Start with a qubit in state 0 (deterministic)
A series of gates are applied, modifying the quantum state to
A measurement operation is performed, collapsing the qubit towards one of the states

## Slide 13: Quantum Circuits
This notion can be extended to a 2-qubit system, capable of encoding 4 different states.
In the general case, quantum circuits are formed by qubits, encoding possible states  Exponential representation!

## Slide 14: Quantum Logical Gates: AND Gate
A double C-NOT (Toffoli) gate is used to entangle qubits and .
Qubit will shift its state only if and are after measurement.
Rotation gates are used to impose superposition in the qubits.
The scheme can be expanded to multiple qubits, generating AND gates will more than two basic events.

## Slide 15: Quantum Logical Gates: OR Gate
The double negation gate assures that at measurement, and are not modified.
The state of will not be modified if prior to the negation gate, and were in state
Extension to multiple qubits is also possible.

## Slide 16
Quantum Encoding of Fault Trees

## Slide 17: Framework to Encode Fault Trees in Quantum Circuits
Blank quantum circuit with qubits, where is number of basic events and number of gates in fault tree
Identify each basic event with a qubit
Apply gates to each basic event, using the following formula to encode the failure probability :
Using quantum gates, replicate the fault tree structure in the quantum circuit
  As the process advances towards the TOP event, the inputs for the gates will be the results from previous gates
Execute the circuit times. Each execution represents one simulation of the fault tree
C
TOP
A
B
D

## Slide 18
Case Study: Dynamic Positioning System

## Slide 19: Dynamic Positioning System (DPS)
DPS can fail due to a power system failure or a computer system failure
Only the computer system has redundancy
As the fault tree is composed by 9 basic events and 5 AND/OR gates, a circuit with 14 qubits will be generated
Basic Event | Annual Failure Probability
Hardware Error | 
Software Error | 
Human Error | 
Power Generation Unit Failure | 
UPS Failure | 
Basic Event | Annual Failure Probability
Hardware Error | 
Software Error | 
Human Error | 
Power Generation Unit Failure | 
UPS Failure | 

## Slide 20: DPS Quantum Circuit

## Slide 21: Results
The circuit is executed 1,000,000 times, obtaining 323,120 failure scenarios
This is in line with the expected failure probability of the system, computed as
From the histogram, those bit-strings corresponding to human errors in the computer system are the most common ones:
  This agrees with the failure probability for human errors being orders of magnitude higher than other basic events
Bit-strings represent system failure
Histogram of Failure Scenarios

## Slide 22: Concluding Remarks
The proposed Quantum Fault Tree successfully encodes the original Fault Tree, mapping the failure probability distribution
Collection of scenarios simulated using the Quantum Fault Tree can provide insights into the weak points of the system, allowing practitioners to take preventive action and allocate resources where they would be more efficient
As the availability and capacity of Quantum hardware grows, it will be possible to encode bigger and more complex trees
Potential speedups and improved assessment of very low probability scenarios