## Slide 1
Automated Fire PRA Scenario Modeling in SAPHIRE Using FRI3D
PSAM 16 – 2022
Steven Prescott
Steven.Prescott@inl.gov
James Knudsen
Stephen Ted Wood
Coauthors

## Slide 2: Fire Risk Analysis
Plant Database
Spatial Information
Walkdown Notes
PRA Model
Fire Simulation Models
Cable Tracing
(Logic Model)
Calculation Methods
Operator Procedures

## Slide 3: Fire Risk Investigation in 3D (FRI3D)
Combine multiple tools and methods to automate many fire PRA tasks
Import existing models/data
Link 3D spatial information
FLASH-CATS
CFAST fire simulation
Calculate component failures
Generate scenarios
Run PRA model

## Slide 4: FRI3D User Interface
Left – Current compartment data
Center – 3D
Right – Trace logic
Bottom – Failure timeline

## Slide 5: FRI3D Automated Scenario Generation
1
Physics Sim
(CFAST)
Determine Failures
(Heat Soak or THIEF calcs.)
Logic for Disabling Components
2
3
4
5
Result Probability
New Scenario
Secondary
Combustibles
(FLASH-CATS)

## Slide 6: How to Do Fire Modeling in SAPHIRE
Initiating Events
Event Trees
Flag Sets
Linkage Rules

## Slide 7: SAPHIRE Fire PRA (Initiating Event)
Step 1 – Create an initiating event for each scenario
Frequency is set to (ignition frequency * non-suppression probability * severity factor)

## Slide 8: SAPHIRE Fire PRA (Event Trees)
Step 2 – Create an event tree for each fire scenario

## Slide 9: SAPHIRE Fire PRA (Target Sets)
Step 3 – Create a flag set for each scenario containing all the scenarios failed basic events being set to a true house event

## Slide 10: SAPHIRE Fire PRA (Linkage Rules)
Step 4 – Add a linkage rule for the even tree to apply the associated Flag set

## Slide 11: SAPHIRE Fire PRA (Solving)
Step 5 – Quantify to fire core damage end state (group under an event tree group for easy access)

## Slide 12: Auto Generating Fire PRA
SAPHIRE MARD
SAPHIRE Macro execution

## Slide 13: SAPHIRE MARD Input
Text-based version of the model
Allows for manual search and replace or software modification
Update new rates for basic events
Comparison

## Slide 14: SAPHIRE Macro Input
Scripts that can be run in SAPHIRE
XML based
Import MARD
Quantify
Generate reports

## Slide 15: FRI3D Demo – Generic PWR Model
Layout for generic PWR
Switch gear room
AFW, SIS, RHR, CCW, 480v cabinets
4KV power
DC power
Cables logic to components

## Slide 16
Video