## Slide 1: Applying a Genetic Algorithm for Finding the Worst Scenario during Post-Disaster Recovery of Water Distribution Networks
Shunichi Tada, Taro Kanno, Kazuo Furuta
the School of Engineering, the University of Tokyo

## Slide 2: Contents
Introduction
Proposed method: Scenario GA
Results & discussion
Conclusion

## Slide 3: Introduction

## Slide 4: Background
Water distribution network (WDN)
- Important infrastructure used by many individuals/organizations.
Fast and efficient recovery during post-disaster period is necessary.
Develop restoration strategies
Evaluate restoration strategies
Train practitioners
Simulation-based optimization
Used for
Issues:
Simple simulation model
Low interpretability of planning
Fixed scenarios
For strategies and training,
Interdependencies with other city functions
High interpretability of planning
Worst assumption among various situations
interpretability & comprehensiveness
Requirements for our simulation:
is critical.

## Slide 5: Simulation of post-disaster recovery of WDNs
Water source
Evacuation site
Civil life
Industry
WDN
Modeling framework of an urban city[1]
Representation of WDN
  : availability rate of lifelines
  : completion rate of companies’ tasks
  : completion rate of citizens’ activities
Evaluation: performance of the city
[1] Kanno, T., Koike, S., Suzuki, T., and Furuta, K. Human-centered modeling framework of multiple interdependency in urban systems for simulation of post-disaster recovery processes. Cogn Tech Work 21, 301–316 (2019).
Branch pipe
Main pipe

## Slide 6: Performance from resilience perspective
t
Performance
Normal state
Sub-system performance(t)
Restoration

## Slide 7: Restoration model and optimization method
Water source
Evacuation site
1
2
3
4
5
6
7
Squad A | 1 | 2 | 5 | 3
Squad B | 4 | 7 | 6 | 
Restoration plan
Heuristic-based optimization[2]: Interpretable strategies
Repair priority
Upstream
Important facility
Main pipe
Many houses
Task assignment
Short duration
Close distance
Area-intensive
Squad A
Squad B
[2] Wakayama, K., Kanno, T., Yuji, K., Takahashi, H., Furuta, K. Comparison of the Post-Disaster Recovery of Water Supply System by GA Optimization and Heuristics. Proceedings of the 30th ESREL and the 15th PSAM Conference, (2020).
Different combination of heuristics = Different strategies

## Slide 8: Objective
Situations surrounding the WDN restoration
Resource scenario
  Restoration squads
  Stockpiles
  Heavy-machineries
Damage scenario
  Number of damaged pipes
  Distribution of damaged pipes
Reflect the real data
Estimated from past events
Uncertain
Develop a method for exploring the worst damage distribution of WDN.
Scenario GA

## Slide 9: Scenario GA

## Slide 10: Scenario GA: overview
We applied the genetic-algorithm (GA) for the scenario exploration.
  One individual = one damage scenario (Number + Distribution)
  Used our previous simulation model and heuristic-based optimization method to calculate individuals’ fitness.
Aims:
  Explore the worst damage scenario.
  Obtain a set of scenarios with various performance. = different difficulties
  Analyze the worse scenarios to obtain bottlenecks.
Utilize for training
Improve strategies

## Slide 11: Scenario GA: genotype and phenotype
Genotype
  Chromosome: one scenario
  Gene: one damaged pipe
Phenotype
  Damaged WDN
Run simulation and get performance.

## Slide 12: Scenario GA: fitness function
In GA, individuals are updated to get individuals with higher fitness.
To explore a scenario with the worst performance (), the fitness is calculated by:
Generation
Fitness
Generation
Performance

## Slide 13: Scenario GA: genetic operators
Operator | Method
Reproduction | Elitism selection Roulette-wheel selection
Crossover | Uniform selection
Mutation | Randomly change genes of randomly selected individual

## Slide 14: Results & Discussions

## Slide 15: Settings
Attributes | Values
Number of pipes | 4610
Number of reservoirs | 1
Number of repair teams | 13
Number of citizens | 6990
- Non-worker citizens | 3064
- Industry worker citizens | 3768
- Lifeline worker citizens | 20
- Repair worker citizens | 105
- Truck worker citizens | 33
Simulation duration | 30 days
Parameters | Values
Length of chromosome | 100
Generation | 100
Population | 100
Rate of elite selection: | 0.2
Rate of roulette wheel selection: | 0.5
Rate of crossover: | 0.3
Rate of mutation: | 0.1
Attributes of the simulation
Parameters of the Scenario GA
Fixed order of heuristics
1. Upstream → 2. Important facility → 3. Main pipe → 4. Many houses
1. Short duration → 2. Close distance → 3. Area intensive
Repair priority
Task assignment

## Slide 16: Result: with worse performance
0.7327: likely to be the worst
Variety of performances

## Slide 17: Discussion: analysis of the obtained scenarios
Area with 5 evacuation sites & 700 citizens
Water source
Squads
#873
#838
Main pipes shared
in the worst scenarios
#838, #873, #961, #1595,
#1979, #2748
#961
#1595
#1979
Closest to squads’ initial position
Closest to the water source
Squads’ initial position
Critical for citizens in the area
Issue:
Current heuristics are not efficient for this situation.
1st prioritized
2nd prioritized
3rd prioritized
Part of WDN

## Slide 18: Result: without worse performance
0.9225: not so bad

## Slide 19: Discussion: exploration efficiency
Search space in this problem:
Parameters of GA exploration:
Generation: 100
Population: 100
Rate of crossover: 0.3
Rate of mutation: 0.1
Only 10000 scenarios were explored.
Most of scenarios were not changed.
Issue:
Need for parameter-tuning

## Slide 20: Conclusion

## Slide 21: Conclusion
Exploration of the worst scenario was successfully done.
Scenarios with different difficulties were obtained.
  They can be utilized for training scenarios
Critical pipes in restoration process were found.
  They can be utilized for improving restoration strategies

## Slide 22: Future studies
Parameter tuning of the Scenario GA
Analysis between bad and good scenarios
Exploration with multiple restoration strategies
Collaboration with the exploration of heuristic

## Slide 23: Thank you for your listening!