## Slide 1
Probabilistic Safety Assessment and Management conference (PSAM)
Planning and evaluation of reliability demonstration tests with uncertainties
Prof. Dr.-Ing. Tobias Leopold

## Slide 2
    Motivation
    Basics of RDT
    Uncertainty in RDT planning
    Case study
    Summary
Agenda
PSAM16
Planning and evaluation of reliability demonstration tests with uncertainties

## Slide 3
Motivation
  Carmakers - recall rate in the United States 1985-2014
Chart: Recall rate
| Hyundai Motor Co | Mitsubishi Motors North America | Volkswagen of America | Volvo Cars of North America | Chrysler Group | American Honda Motor Co | Ford Motor Co | BMW of North America | Toyota Motor Corp | Kia Motors | Subaru of America | Nissan North America | General Motors | Mazda Motor Corp | Mercedes-Benz USA
Recall rate | 1.15 | 1.09 | 1.06 | 1.05 | 1 | 0.94 | 0.93 | 0.9 | 0.8 | 0.77 | 0.73 | 0.71 | 0.65 | 0.55 | 0.41
Source: https://www.statista.com/statistics/309633/number-of-recalls-per-sale-for-car-manufacturing-groups-in-the-us/

## Slide 4
  Appropriate reliability target on system level
  derived reliability targets on subsystem, assembly, module and component level
  Definition of suitable load spectra
  Confidence level of reliability proof
   Failure-free or failure-oriented reliability testing?
Basics of RDT: Precondition – Reliability Target

## Slide 5
  Planning based on binomial-distribution
          : confidence level
          : minimum reliability
          : service life requirement
          : sample size
          : number of failed specimen
  RDT aims at testing without failures
          highest confidence level is achieved or the smallest sample size is required
Basics of RDT

## Slide 6
  Testing without failures – success run
          : confidence level
          : minimum reliability
          : service life requirement
          : sample size
  No assumption of a specific failure distribution required
   Test planning appears simple
   Appears attractive especially with low experience knowledge!
Basics of RDT

## Slide 7
  Testing longer or shorter than the service life  life time ratio
  With the assumption of a Weibull-distributed failure characteristic
          : shape parameter of the Weibull distribution
  Good integration of project boundary conditions possible, e.g. test duration or available number of test items
  Assumption of a specific failure distribution is required!
Basics of RDT

## Slide 8
  What is the size of the shape parameter ?
  Can only be determined from failure data!
  Possibilities of estimation
          predecessor products
          stochastic lifetime simulation
          …
          A look into literature? „… for example = 2.0“
   Investigation of uncertain estimation in a case study …
Uncertainty in RDT planning – estimation of shape parameter

## Slide 9
  Probability for a successful life test
  With the assumption of a Weibull-distributed failure characteristic
          : shape parameter of the Weibull distribution
          : scale parameter of the Weibull distribution
  Easy planning of a RDT is depending on the estimation of the failure behavior of the product!
Uncertainty in RDT planning – probability for successful test

## Slide 10
   Investigation of an uncertain estimation in a case study …
  B10 = 100.000 LC, confidence level CL= 90%
  Scenario I: LR = 0.75  possible test duration of 75.000 LC
  Scenario II: LR = 0.50  possible test duration of 50.000 LC
Case study – overview

## Slide 11
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
Case study – effect of uncertain shape parameter

## Slide 12
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
Case study – effect of uncertain shape parameter

## Slide 13
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
Case study – effect of uncertain shape parameter

## Slide 14
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
Case study – effect of uncertain shape parameter

## Slide 15
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
Case study – probability of sucessful life test
correct test planning without uncertainties

## Slide 16
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
 | assumption | reality
shape parameter | 3.0 | 2.5
scale parameter | 800.000 LC | 400.000 LC
sample size | 52 | 52
probability of success | 95.8% | 45.3%
 | assumption | reality
 | 3.0 | 2.5
 | 800.000 LC | 400.000 LC
 | 52 | 52
 | 95.8% | 45.3%
Case study – probability of sucessful life test
test planning with uncertainties

## Slide 17
  B10 = 100.000 LC, confidence level CL = 90%
  Scenario I: 75.000 LC
  Scenario II: 50.000 LC
 | assumption | reality
shape parameter | 3.0 | 2.5
scale parameter | 800.000 LC | 400.000 LC
sample size | 175 | 175
probability of success | 95.8% | 38.0%
 | assumption | reality
 | 3.0 | 2.5
 | 800.000 LC | 400.000 LC
 | 175 | 175
 | 95.8% | 38.0%
Case study – probability of sucessful life test
test planning with uncertainties

## Slide 18
  Failure behavior must be understood and sufficiently describable
  Original assumptions must be verified, especially regarding the shape parameter
          e.g. success run test for release of a sample phase
          after this release, the life test is continued until test specimen fail
          Using this failure date to estimate the shape parameter
  Incorrect estimation can lead to risk in product release  potential field issue with cost risk
Summary

## Slide 19
   Better investing in product reliability testing than in field campaigns!
Appeal for the Future

## Slide 20: THANK YOU VERY MUCH FOR YOUR ATTENTION!
Visit us at:
WWW.HS-ESSLINGEN.DE/EN