## Slide 1: Dynamic Probabilistic Risk Assessment for Cyber Security Risk Analysis in Nuclear Reactors.
Pavan Kumar Vaddi, Yunfei Zhao, and Carol Smidts
Department of Mechanical and Aerospace Engineering, The Ohio State University.
June 30, 2022.

## Slide 2: Introduction
Objectives of PRA:
Identify “what can go wrong”
  identifying the initiating events and the possible sequences of events that can result in undesirable consequences.
Identify and Establish “what are the consequences if something went wrong”
  identifying and evaluating the above-mentioned potentially risky consequences when the initiating events occur and evolve.
Quantify “how likely it is for something to go wrong”
  computing the likelihood of occurrence of the above-mentioned initiating events and the probabilities that those initiating events evolve into said dangerous scenarios
A. Mosleh, “PRA: A PERSPECTIVE ON STRENGTHS, CURRENT LIMITATIONS, AND POSSIBLE IMPROVEMENTS,” Nucl. Eng. Technol., vol. 46, no. 1, pp. 1–10, Feb. 2014, doi: 10.5516/NET.03.2014.700.
R. J. Breeding, T. J. Leahy, and J. Young, “Probabilistic risk assessment course documentation. Volume 1: PRA fundamentals,” Energy, Inc., Seattle, WA (USA), NUREG/CR-4350/1; SAND-85-1495/1, Aug. 1985. doi: 10.2172/6277413.

## Slide 3: Introduction
Initiating events:
“any event that creates a disturbance in the plant that has the potential to lead to core damage, depending on the successful operation of the required mitigation systems in the plant.”
Component failures – mechanical or software.
Operator errors.
Cyber-attacks.
International Atomic Energy Agency, “Defining initiating events for purposes of probabilistic safety assessment,” IAEA-TECDOC-719, International Atomic Energy Agency. 1993.

## Slide 4: Elements of Cyber-Attack on ICS
The ICS under attack
Digital Components
Physical Components
Physical World
Defender / Operator
Attacker
“interaction” between the attacker and the defender
Manual Control

## Slide 5: Introduction
Dynamic Probabilistic Risk Assessment
A set of probabilistic risk assessment techniques that uses deterministic physics based dynamic models of the system to study its evolution in the context of random events.
Advantages of DPRA:
  Modeling and incorporating the changes in system properties as functions of physics and time. ex: failure rates.
  Modeling the changes in the behaviour of human operators with respect to system states and time.
  Capturing the evolution of the system over time due to random events.*
  Modeling the changes in the behaviour of attackers and defenders (operators) with respect to system states and time.
J. Devooght and C. Smidts, “Probabilistic Reactor Dynamics—I: The Theory of Continuous Event Trees,” Nucl. Sci. Eng., vol. 111, no. 3, pp. 229–240, Jul. 1992, doi: 10.13182/NSE92-A23937.
T. Aldemir, “A survey of dynamic methodologies for probabilistic safety assessment of nuclear power plants,” Ann. Nucl. Energy, vol. 52, pp. 113–124, Feb. 2013, doi: 10.1016/j.anucene.2012.08.001.

## Slide 6: DPRA and Elements of Cyber-Attack on ICS
The ICS under attack
Digital Components
Physical Components
Physical World
Defender / Operator
Attacker
Existing DPRA techniques

## Slide 7: DPRA and Elements of Cyber-Attack on ICS
The ICS under attack
Digital Components
Physical Components
Physical World
Defender / Operator
Attacker
Proposed DPRA framework
“interaction” between the attacker and the defender

## Slide 8: Theory of Continuous Event Trees – System Description
- A vector representing the physical state of a nuclear power plant.
  Vector of physical variables such as pressure, flowrate, temperature etc.
  is a point in continuous space with its boundaries determined by system physics.
  represents the space of all possible physical state vectors .
- The states of the components in the NPP are represented using a discrete vector. represents the set of all possible component states.
The couple represents the latest pair of actions taken by the defender and the attacker respectively. is the defender’s action space. is the attacker’s action space. We assume that the defender and the attacker action spaces are discrete.
At any time , the overall system state of the NPP is represented using the tuple .

## Slide 9: Theory of Continuous Event Trees – System Description
- The states of the components in the NPP are represented using a discrete vector.
For example, we can use integers to represent discrete states of components.
  0 – Normal, 1 - Failed, 2 – Compromised.
For the example system, , where
Controller (1)
Mechanical Valve (3)
Digital flow sensor (2)

## Slide 10: Theory of Continuous Event Trees - Trajectories
,
time
Assume that the solution to the above equation is .
Trajectory is dependent on , which in turn depends on physics (component failures), and the actions of the defender and the attacker .
Trajectories in state space
J. Devooght and C. Smidts, “Probabilistic Reactor Dynamics—I: The Theory of Continuous Event Trees,” Nucl. Sci. Eng., vol. 111, no. 3, pp. 229–240, Jul. 1992, doi: 10.13182/NSE92-A23937.

## Slide 11: Theory of Continuous Event Trees
= The conditional probability that there is a transition out of the substate ( in the interval , when the system is in state .
= The conditional probability that the component state transitions from to in the interval explicitly due to random component failures when the physical state vector is and the defender and attacker take no new actions.
= The conditional probability that the component state transitions from to in the interval when the defender and attacker take new actions and respectively at the physical state .
The probability that the system evolves along the trajectory defined by without leaving the substate between time and is

## Slide 12: Theory of Continuous Event Trees
= Unsafe region in state space
= Safe region in state space
= the probability density of the overall system stateat time .

## Slide 13: Theory of Continuous Event Trees
The conditional probability density that the system is in state given the initial state , denoted by
If the overall system state is initially, then the probability density that the system reaches the physical state at time while remaining in the substate until time is given by the product
time
J. Devooght and C. Smidts, “Probabilistic Reactor Dynamics—I: The Theory of Continuous Event Trees,” Nucl. Sci. Eng., vol. 111, no. 3, pp. 229–240, Jul. 1992, doi: 10.13182/NSE92-A23937.

## Slide 14: Continuous Event Trees – Extended to Cyber-Attacks

## Slide 15: Continuous Event Trees – Extended to Cyber-Attacks
This represents the probability density that the system is initially in the state (, and reaches the physical state at time while remaining in the substate until time , along the trajectory defined by .
time

## Slide 16: Continuous Event Trees – Extended to Cyber-Attacks
time
(
(
the system is in state at some intermediate time between and ,
the component state transitions from to due to a random event and not due to attacker and defender actions, at time
after that the system evolves along the trajectory defined by while remaining in the state from time to ,
Eventually reaches the physical system state at time

## Slide 17: Continuous Event Trees – Extended to Cyber-Attacks
time
(
(
the system is in state at some intermediate time between and ,
the defender and the attacker take new actions as a result of which the component state transitions from to
after that the system evolves along the trajectory defined by while remaining in the state from time to ,
Eventually reaches the physical system state at time

## Slide 18: Continuous Event Trees
Trajectory
Trajectory 2
Initiating event
time
J. Devooght and C. Smidts, “Probabilistic Reactor Dynamics—I: The Theory of Continuous Event Trees,” Nucl. Sci. Eng., vol. 111, no. 3, pp. 229–240, Jul. 1992, doi: 10.13182/NSE92-A23937.

## Slide 19: CETs and DDETs
time
If we discretize the timeline and explore all possible* transitions at every time-step, then CET converts into a discrete Dynamic Event Tree.

## Slide 20
Defender / Operator
Attacker
“interaction” between the attacker and the defender
Continuous Event Trees – Extended to Cyber-Attacks
Modeled using Stochastic Games.
Two players: attacker and defender.
is the set of system states.
is the defender’s action space and is the attacker’s action space.
and are the action policies of the defender and the attacker.
is the state transition probability mapping.
is the reward function of the defender.
is the attacker’s reward function.

## Slide 21: Continuous Event Trees – Extended to Cyber-Attacks
Equation to calculate reward functions:

## Slide 22: Continuous Event Trees – Extended to Cyber-Attacks
is the cost incurred by the defender for taking the action at the physical system state , the component state and time .
is the cost incurred by the attacker for taking the action at the physical system state , the component state and time .
The expected immediate reward received by the player when there is a transition out of the component state due to the pair of actions .
The term is the immediate reward received by the player , when the component state transitions from to due to the pair of actions , where is the probability of that transition.

## Slide 23: Continuous Event Trees – Extended to Cyber-Attacks
Recursive equation to compute rewards from future states.
The term represents the reward received by the player at some future state at time , physical system state and component state , when the defender takes action and the attacker takes an action .
The term represents the conditional probability density of arriving at the system state given that the initial state is ).

## Slide 24
DPRA Engine
Action model
System model
System physical state and component state information
Sampled attacker and operator actions
Sampled component failures.
Possible attacker and defender actions
Post processing module
Data for analysis
DPRA Simulation Architecture

## Slide 25
DPRA Engine
Sampler
Scheduler
Data Collection module
Component Failure Models of NPP Components
System physical state and component state information.
Possible attacker and defender actions
System model
Action model
Updated failure rates and failure modes
sampled transition time, sampled state transition, and sampled actions.
DPRA Engine

## Slide 26
Monitoring information from sensors
Control commands to actuators
Monitoring information from sensors to auxiliary operator
Control commands from auxiliary operator to actuators
Communication between control systems layer and data historians.
Communication between HMI and data historians.
Communication between HMI and control systems layer.
Communication between HMI and operator in control room.
Network data and sensor information
(All colors) Communication layer between two subsystems
System Model

## Slide 27: Action Model
Undetected Attacker Model
System Model
Game model
Action Model
DPRA Engine
Observations from system
Attack detected
End of attack
Set of possible actions
Procedure Model

## Slide 28
Game
Attacker Model
Defender Model
Spinoff DPRA
Game model
System state information
Set of possible attacker and defender actions.
Game Model

## Slide 29: Conclusions
We formalized the continuous event trees framework in the context of cyber-attacks.
  We presented Chapman-Kolmogorov based equations to quantify the probability density that the system is in a given state at any point of time.
We proposed a simulation architecture to implement the extended CETs for cybersecurity risk analysis.

## Slide 30: Thank You
Acknowledgements
This research is being performed using funding received from the DOE Office of Nuclear Energy's Nuclear Energy University Program.