## Slide 1: Impact of Correlation between Performance Shaping Factors on Their Multipliers
Yusuke Takao, Satoshi Takeda, Takanori Kitada
Osaka University
PSAM 16
Y-233
Notes: Thank you for the introduction.
I’m Yusuke Takao from Osaka University in Japan.
Today I’d like to talk about (title).

## Slide 2: Outline
*one of the Human Reliability Analysis methods
Background & Purpose
Review of SPAR-H*
Background of SPAR-H, definition of complexity and stress
Method
How to calculate multiplier considering correlation
Result
The impact of correlation between PSFs on multiplier
Discussion
Summary
Notes: This is the outline of my presentation. This presentation is divided into 6 parts.
First, I will talk about the background and purpose of this research.
Second is the review of SPAR-H, which is one of the Human reliability Analysis methods. And we used this method in this research. In this part, I will introduce the background of SPAR-H, and definition of complexity and stress among all Performance Shaping Factors.
Third, I will introduce the method how to calculate multiplier considering correlation and then the result of this research. In result, we evaluated the impact of correlation between PSFs on multiplier.
After that I will discuss about this research, and lastly, I will introduce summary of this presentation.

## Slide 3: Background
About 80% of accidents that occur at Nuclear Power Plant (NPPs) are caused by human error1).
Human Reliability Analysis (HRA) quantitatively identifies and analyzes the causes of human error by calculating Human Error Possibility (HEP).
SPAR-H is one of HRA methods and it calls factors that may influence human activities Performance Shaping Factors (PSFs).
IAEA, (2013). Managing Human Performance to Improve Nuclear Facility Operation
Notes: So, let’s start from the background of this research.
Since the accident at Fukushima, there has been a growing awareness of the need to reduce the risk of accidents at nuclear power plants (NPPs).
About 80% of accidents that occur at Nuclear Power Plant (NPPs) are caused by human error1) , this indicate that it is important to evaluate human error appropriately.
Human Reliability Analysis (HRA) quantitatively identifies and analyzes the causes of human error by calculating Human Error Possibility (HEP).
SPAR-H is one of HRA methods and it calls factors that may influence human activities Performance Shaping Factors (PSFs).

## Slide 4: Purpose
Generally, PSFs are treated as independent but PSFs have been reported to have correlations2,3).
The correlation coefficients of PSFs have been evaluated from accident report in Korean NPPs4).
To evaluate the impact of the correlation on the multiplier.
Purpose
2) Boring, R.L., How Many Performance Shaping Factors Are Necessary for Human Reliability Analysis? 2010, Idaho National Laboratory (INL).
3) Jianqiao Liu et al, Analysis of dependencies among performance shaping factors in human reliability analysis based on a system dynamics approach. Reliability Engineering & System Safety 215(2021)107890
4) Jooyoung Park et al, Inter-relationships between performance shaping factors for human reliability analysis of nuclear power plants. Nuclear Engineering and Technology 52(2020)87-100
Notes: Generally, PSFs are treated as independent but PSFs have been reported to have correlations2,3).
And, HEP may significantly change by considering correlation.
The correlation coefficients between PSFs have been evaluated from accident report in Korean Nuclear Power Plants4).
From this perspective, the purpose of my research is to evaluate the impact of the correlation on the multiplier.

## Slide 5: Review of SPAR-H -Background of SPAR-H
SPAR-H simplifies and generalizes the approach of the THERP method5).
SPAR-H method considers 8 PSFs, and each PSFs has level and corresponding multipliers.
Increase HEP
Decrease HEP
5) L. Boring, S. Blackman. “The origins of the SPAR-H method’s performance shaping factor multipliers.” 2007 IEEE 8th Human Factors and Power Plants and HPRCT 13th Annual Meeting, pp. 177-184, (2007)
PSFs used in SPAR-H：
Available time, Stress, Complexity, Experience/Training, Procedures, Ergonomics/HMI, Fitness for duty, Work Processes
Notes: From this slide, I will introduce the review of SPAR-H method. This slide shows the background of SPAR-H.
SPAR-H is an HRA method developed by Idaho National Laboratory in 1994.
SPAR-H simplifies and generalizes the approach of the THERP method, which is main method used in Japanese NPPs.
SPAR-H considers 8 PSFs, such as available time, stress, complexity and so on. And each PSFs has level and corresponding multipliers. The multipliers used in SPAR-H are established based on THERP, but the data base used in THERP method is not clear well. SPAR-H considers that PSFs not only increase HEP but also decrease HEP.
The table below is example of the level and multiplier of the PSF.
Look at complexity. There are 4 levels and corresponding multipliers.
When the level is highly complex or moderately complex, the multiplier is larger than 1, which means that complexity increases HEP.
However, when the level of complexity is obvious diagnosis, the multiplier is smaller than 1, which means that complexity decreases HEP.
Then look at stress. There are 3 levels and corresponding multipliers. When the level is Extreme or High, Stress increases HEP, and there are no levels that stress decreases HEP.
Other PSFs have levels and corresponding multipliers as well as them.
From the next slide, I will introduce why we used stress and complexity in this research.

## Slide 6: Review of SPAR-H -Definition of Stress
The degree of undesirable conditions or situation that prevent the operator from completing a task easily6).
Stress includes mental stress, excessive workload and physical stress.
Stressors such as noise and poor ventilation may cause mental or physical stress to operator.
Level for Stress | Explanation | Multiplier
Extreme | Regrade the performance of operators. Stressor suddenly happens and stressful situation lasts long time. | 5
High | Lower than extreme level. | 2
Nominal | Conductive to good performance | 1
Stress
6) Idaho National Laboratory, The SPAR-H Human Reliability Analysis Method
Notes: This slide shows the definition of Stress. Stress means the degree of undesirable conditions or situation that prevent the operator from completing a task easily. Stress includes mental stress, excessive workload and physical stress. Stressors such as noise and poor ventilation may cause mental or physical stress to operator.
The table below shows the level for stress.
Extreme stress regrades the performance of operators. And this is when stressor suddenly happens, and stressful situation lasts long. The corresponding multiplier is 5.
High stress is lower than extreme level and the multiplier is 2. In nominal level, operators conduct to good performance and multiplier is 1.
This is the definition of stress.

## Slide 7: Review of SPAR-H -Definition of Complexity
Difficulty of performing a task in the given situation.
SPAR-H considers 14 contributing factors to complexity,
parallel tasks, mental calculation required, etc.
Level for Complexity | Explanation | Multiplier
Highly complex | Very difficult to perform a task. Many variables are involved. | 5
Moderately complex | Somewhat difficult to perform. Several variables are involved. | 2
Nominal | Not difficult to perform. Single or few variables are involved. | 1
Obvious diagnosis | Diagnosis becomes greatly simplified. There are much times to diagnosis . | 0.1
Complexity
A lot of parallel tasks may cause stress on operator.
Notes: This slide shows the definition of the complexity. Complexity is difficulty of performing a task in a given situation.
SPAR-H considers 14 contributing factors to complexity, such as parallel tasks, large number of actions required, and also mental effort required such as performing mental calculations.
The table below is introduction of level for complexity.
Highly complex means very difficult to perform a task, and there are many variables involved. The corresponding multiplier is 5.
Moderately complex means somewhat difficult to perform, and there are several variables involved. The multiplier in this level is 2.
Nominal means not difficult to perform, and single or few variables are involved. The multiplier is 1.
In obvious complex level, diagnosis becomes greatly simplified, and there are much time to diagnosis. The multiplier in this level is 0.1.
We can imagine that high complexity situation leads to high stress situation. For example, when there are a lot of parallel tasks, operator may get stressed. From this point, there seem to be correlation between Stress and Complexity.

## Slide 8
There seem to be correlation between stress and complexity.
The coefficients between stress and complexity is 0.5884), which is relatively strong.
Evaluate the impact of correlation on multiplier using stress and complexity.
Review of SPAR-H -Definition of Stress and Complexity
4) Jooyoung Park et al, Inter-relationships between performance shaping factors for human reliability analysis of nuclear power plants. Nuclear Engineering and Technology 52(2020)87-100
Notes: As I said in the last slide, there seem to be correlation between stress and complexity.
And the correlation coefficients of them calculated from Korean NPPs is 0.588, which is relatively strong.
From these points, we evaluated the impact of correlation on multiplier using stress and complexity in this research.

## Slide 9: Method
The influence of complexity is reduced by the influence of stress on the HEP.
There is a correlation in the large amount of empirical data used to calculate the multiplier for PSFs.
Premise
The influence of complexity is strong
HEP increases 5 times
Chart: 
| independent
complexity | 5 | 0
stress | 0 | 0
Chart: 
| independent | correlation
complexity | 1 | 0.65
stress | 0 | 0.35
The influence of stress is increased by considering correlation.
Influence of complexity considering correlation.
Notes: From this slide, I will introduce the method how to calculate multiplier considering correlation. We premised that there is a correlation in the large amount of empirical data used to calculate the multiplier for PSFs.
This graph below shows the image of our method and the percentage of influence by PSFs, in the situation where the influence of complexity is strong and Human Error Possibility increases 5 times.
When we consider that PSFs are independent, the percentage of Complexity is 100% and the multiplier can be set 5 in this situation.
However, when we consider that complexity and stress have correlation (click), the influence of stress is increased by considering correlation (click), and HEP increases 5 times including the influence of stress on HEP.
Rejecting the influence of stress (click), we can obtain the multiplier of complexity considering correlation in this situation, which is smaller than 5.
From this point (click), the influence of complexity is reduced by the influence of stress on the HEP.
In the next slide, I will explain how to calculate multiplier considering correlation.

## Slide 10: Method
: expected value (=1)
, : standard deviation
: correlation coefficient
Multiplier
considering correlation
satisfies
Conditional expectation
The multipliers follow a normal distribution.
The standard deviations of PSFs are equal.
The influence of PSF[A],[B] are strong, and HEP increases N times.
Notes: In order to calculate multiplier considering correlation, we assumed that the multiplier of PSFs follow a normal distribution which expected value is 1. And we also assumed that the standard deviations of PSFs are equal.
Let us consider a situation where the influence of PSF[A],[B] are strong and the HEP increases N times by using their multiplier . Finally, we calculate which is multiplier of PSF[A] considering correlation.
In this situation, satisfies this expression. So, the product of them is N.
When turns to , the conditional expectation of is like this expression. refer the expected values and , are standard deviations. refers the correlation coefficients between PSF[A] and [B].
Summarizing these expressions, we obtain that is multiplier considering corelation of PSF[A].
This is how to calculate multiplier considering correlation in this method. In the next slide, I will show you the result of our research.
In order to calculate multiplier considering correlation, we assumed that the multiplier of PSFs follow a normal distribution which expected value is 1. And we also assumed that the standard deviations of PSFs are equal.
Let us consider a situation where the influence of PSF[A],[B], among 8 PSFs are strong and the HEP increases N times. Finally, we calculate the conditional expectation 𝑥_𝐴′〖,𝑥〗_𝐵′ considering correlation.
In this situation, 𝑥_𝐴′〖,𝑥〗_𝐵′ satisfies (1).
When 𝑥_𝐴 turns to 𝑥_𝐴′, the conditional expectation of 𝑥_𝐵 is (2).
Summarizing (1)(2), we obtain 𝑥_𝐴′ of PSF[A] considering correlation.

## Slide 11: Result
Multiplier changes 0.52 ~ 1.90 times considering correlation.
The correlation between PSFs could have significant impact on multiplier.
M | M’ | M’/M
5 | 2.59 | 0.52
2 | 1.53 | 0.77
1 | 1 | 1
0.1 | 0.19 | 1.90
M’: Multiplier considering correlation, M’/M: the ratio of M to M’
Notes: In this slide, I will explain the result of this research.
The table below shows the multiplier used in Stress and Complexity.
M is the original multiplier used in SPAR-H. M’(M prime) refers the multiplier considering correlation. M’/M is the ratio of M to M’.
When M is 5, multiplier change by half considering correlation. When M is 2, multiplier change 0.77 times. However, when M is 0.1, multiplier change by 2 times. So, Multiplier changes from 0.52 to 1.90 times considering correlation.
The reason why the multipliers change considering correlation is that the influence on HEP is reduced by considering correlation. When multiplier of complexity is 5, the influence of complexity is reduced by stress in the same situation that increase HEP 5 times. This explanation is applicable when the multiplier is 2 or 0.1.
From this result, it is obvious that the correlation between PSFs could have significant impact on the multiplier, and also on HEP.

## Slide 12: Discussion1
Chart: Correlation coefficients
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
M=5 | 5 | 3.8815 | 3.3852 | 3.0792 | 2.8642 | 2.7016 | 2.5726 | 2.4669 | 2.3781 | 2.3021 | 2.2361
The multiplier considering uncertainty of correlation coefficients.
Discussion
Correlation coefficients:
0.588
The change of the multiplier is small even when we consider the uncertainty in correlation coefficients.
Notes: From this slide, I want to discuss about our research. There are 3 discussions.
First, I want to evaluate multiplier considering uncertainty of correlation coefficients.
The reason why we considered the uncertainty of the correlation coefficients is that we can imagine that the coefficient may depend on country, culture, and differ for human. So there seem to be uncertainty in correlation coefficients.
This graph shows the change of the multiplier in the case when the original multiplier is 5. And the red point shows the correlation coefficient that is calculated form accident report in Korea.
As you can see in this figure, the change of multiplier around 0.588 is small.
This indicates that the change of the multiplier is small even when we consider the uncertainty in correlation coefficients.

## Slide 13: Discussion2
Assume that multiplier follow a log normal distribution
Evaluate the impact on the multiplier considering different distributions.
Discussion
When the multipliers follow a normal distribution, the multiplier take negative values. But multipliers don’t take negative value.
Problem
Notes: From this slide, I will introduce the second discussion.
In our research, there is a problem; when the multipliers of PSFs follow a normal distribution, the multiplier take negative values. But multipliers only take positive value, and don’t take negative value.
So, in this discussion, we assume that multiplier follow a log normal distribution, and evaluate the impact on the multiplier considering different distribution that multipliers follow.

## Slide 14: Discussion2
The difference of impact on multiplier between distributions is small.
Comparison of calculation
Normal distribution
Log normal distribution
Multiplier | M’ | M” | M”/M’
5 | 2.59 | 2.61 | 1.01
2 | 1.53 | 1.47 | 0.96
1 | 1 | 1 | 1
0.1 | 0.19 | 0.22 | 1.16
M’: normal distribution, M”: log normal distribution
Notes: The method how to calculate the multipliers considering correlation when they follow a log normal distribution is same that when they follow a normal distribution.
This shows the comparison of the multiplier calculation between normal distribution and log normal distribution, in the situation where the influence of PSF[A] is strong and HEP increases N times.
One of the difference between them is that is logarithmic conversion. This means that takes only positive value.
The table below shows the result of this discussion. M’(M prime) refers the multipliers considering correlation when they follow a normal distribution. M”(M double prime ) shows the multiplier considering correlation when they follow a log normal distribution.
When M is 5, the ratio of M” and M’ is 1.01. When M is 2, the ratio is 0.96. And, when M is 0.1, the ratio is 1.16. So, the range of ratio is from 0.96 to 1.16.
This result indicate that the impact on the multiplier considering different distribution is small.
The method how to calculate the multipliers when they follow a log normal distribution is same that when they follow a normal distribution.
We consider a situation where the influence of PSF[A],[B], among 8 PSFs are strong and the HEP increases N times, and calculate the conditional expectation 𝑥_𝐴′〖,𝑥〗_𝐵′ considering correlation.
And summarizing the 2 expression, we obtain multiplier considering correlation in this assumption.
The table below shows the result of this discussion. M refers the multiplier used in SPAR-H. M’ refers the multiplier considering correlation assuming that multiplier follow a normal distribution. M” shows the multiplier considering correlation assuming that multiplier follow a log normal distribution.

## Slide 15: Discussion3
Evaluate the impact of correlation on HEP.
Discussion
Consider a situation that a task is diagnosis part.
The base HEP (NHEP) is 0.01.
Modify the NHEP considering 8 PSFs.
Method
HEP=（NHEP）×）
Notes: In the last discussion, we evaluate the impact of correlation between PSFs on HEP.
The method how to calculate HEP in SPAR-H is here. Let us consider a situation where a task is thought to be diagnosis part. The base HEP (NHEP) ,which is average in diagnosis part, is 0.01. And modify the NHEP considering 8 PSFs like the formula below. So HEP is the product of NHEP and multipliers of all PSFs.

## Slide 16: Discussion3
PSF | Multiplier | 
 | Original | Considering correlation
Complexity | 2 | 1.53
Stress | 5 | 2.59
Other PSFs | 1 | 1
NHEP | 0.01 | 0.01
HEP | 0.10 | 0.04
HEP is about -60% considering correlation.
Complexity and stress affect on HEP and other PSFs are nominal.
Situation
Notes: We considered a situation where the multiplier of complexity and stress are 2 and 5 respectively, and other PSFs are nominal level. In this discussion, we assumed that multipliers follow a normal distribution. The result is in the table below.
In the original calculation, the product of all PSFs multipliers is 10, and HEP is 0.1 in this situation. However, when we consider the correlation between PSFs, the multipliers of complexity and stress are decreased, and HEP is 0.04. Comparing 2 HEPs, HEP is about -60% considering correlation. This indicate that correlation between PSFs could have significant impact on HEP.
When HEP change like this scenario, the priority of risk may change. So, calculating HEP appropriately is important in HRA.

## Slide 17: Summary
The correlation coefficients between PSFs used in SPAR-H have been reported.
Correlation coefficient between complexity and stress is 0.588, and the correlation exist in practice.
  Evaluated the impact of correlation between complexity and stress on the multiplier.
The multipliers change from 0.52 to 1.90 times considering correlation.
  The correlation between PSFs could have significant impact on the multiplier and HEP.
Notes: This is summary of my research.
Since the accident at Fukushima, there are growing awareness of the need to reduce the risk at NPPs.
SPAR-H, one of the HRA method, have eight PSFs that affect human activities. The correlation coefficients between PSFs have been reported, and HEP may significantly change by considering correlation.
The correlation coefficient between complexity and stress is 0.588, and there seem to be correlation in practice. From this point, we evaluate the impact of correlation between complexity and stress on the multiplier.
At the result of this research, we found that multipliers change from 0.52 to 1.9 times, this indicate that the correlation between PSFs could have significant impact on the multiplier, and also on HEP.
This is the end of my presentation. Thank you for listening.

## Slide 18: Future tasks
Calculate the correlation coefficients using accident report at NPPs in Japan.
Improve the formula of HEP considering correlation.

## Slide 19: Appendix: correlation coefficients
 | Ergonomics/HMI | Available Time | Procedures | Work Processes | Complexity | Experience/ Training | Stress/ Stressors | Fitness For duty
Ergonomics/ HMI | R = 1.0 |  |  |  |  |  |  | 
Available time | 0.283 | 1.0 |  |  |  |  |  | 
Procedures | 0.367 | 0.313 | 1.0 |  |  |  |  | 
Work processes | 0.323 | 0.467 | 0.604 | 1.0 |  |  |  | 
Complexity | 0.376 | 0.524 | 0.413 | 0.526 | 1.0 |  |  | 
Experience/ Training | 0.418 | 0.350 | 0.646 | 0.475 | 0.458 | 1.0 |  | 
Stress/Stressors | 0.127 | 0.651 | 0.288 | 0.379 | 0.588 | 0.379 | 1.0 | 
Fitness for duty | -0.046 | 0.297 | 0.178 | 0.137 | 0.417 | 0.201 | 0.593 | 1.0

## Slide 20: Appendix: PSFs
PSF | PSF Level | Multiplier（Diagnosis） | Multiplier（Action）
Available time | Inadequate time | HEP=1.0 | HEP=1.0
 | Barely adequate time | 10 | 10
 | Nominal time | 1 | 1
 | Extra time | 0.1 | 0.1
 | Expansive time | 0.01 | 0.01
Stress | Extreme | 5 | 5
 | High | 2 | 2
 | Nominal | 1 | 1
Complexity | Highly complex | 5 | 5
 | Moderately complex | 2 | 2
 | Nominal | 1 | 1
 | Obvious diagnosis | 0.1 | -
Experience/ Training | Low | 10 | 3
 | Nominal | 1 | 1
 | High | 0.5 | 0.5

## Slide 21: Appendix: PSFs
PSF | PSF Level | Multiplier（Diagnosis） | Multiplier（Action）
Procedures | Not available | 50 | 50
 | Incomplete | 20 | 20
 | Available, but poor | 5 | 5
 | Nominal | 1 | 1
 | Diagnostic/symptom oriented | 0.5 | 
Ergonomics/HMI | Missing/Misleading | 50 | 50
 | Poor | 10 | 10
 | Nominal | 1 | 1
 | Good | 0.5 | 0.5
Fitness for duty | Unfit | HEP=1.0 | HEP=1.0
 | Degraded Fitness | 5 | 5
 | Nominal | 1 | 1
Work Processes | Poor | 2 | 5
 | Nominal | 1 | 1
 | Good | 0.8 | 0.5

## Slide 22: Appendix: How to calculate the correlation coefficients
If the event report mentioned that a PSF contributed to human errors, the PSF was coded as “1” on the spreadsheet; if not, it was coded as “0.”
“Phi correlation coefficient” that represents a measure of the degree of correlation between two binary variables is applied to calculate the correlation coefficients.
PSFs | Available time (influence) | Available time (not influence) | Total
Stress (influence) | X | 11-X | 11
Stress (not influence) | 10-X | 43+X | 53
Total | 10 | 54 | 64
Notes: X refers the number where both of stress and available time influence on human error.

## Slide 23: Appendix: the priority of scenario
Chart: 
| independent | correlation
scenario 1 | 0.03 | 0.01
scenario 2 | 0.02 | 0.015
When considering correlation, the priority between scenarios may change.
-60%
-25%
Notes: In scenario 1 and 2, the different PSFs affect on HEP, and the amount of reduction considering correlation is different. When we consider that HEP decrease about -60% in scenario1, and -25% in scenario2 considering correlation, the priority changes.

## Slide 24: Appendix: consider the difference of standard deviation
The number of multipliers set in the PSF is small, this makes it difficult to set an appropriate standard deviation.
Establish ratios of standard deviations between stress and complexity.
PSF | PSF : Stress
Available time | 
Complexity | 
Experience/Training | 
Procedures | 
Ergonomics/HMI | 
Fitness for duty | 
Work processes | 
PSF | PSF : Stress
Available time | 
Complexity | 
Experience/Training | 
Procedures | 
Ergonomics/HMI | 
Fitness for duty | 
Work processes | 
Notes: The difference of range of multiplier between Stress and Complexity is small, so we assumed that the standard deviation of them is same.

## Slide 25: Appendix: Correlation between 2 or more PSFs
The correlation exist in Stress.
The influence of all PSFs are strong, and HEP increases N times.
Stress: PSF[S], Other PSFs: PSF[A]~[G]
Situation
Conditional expectation
Substitution:
obtain multiplier of stress considering correlation
Notes: The correlation between 2 or more PSFs. The influence of all PSFs are strong, and HEP increases N times. PSF[S] refers Stress, and PSF[A]~[G] refer the other PSFs.
We consider a situation where all 8 PSFs influence on HEP, and HEP increases N times. And finally, calculate ’ which is multiplier of stress considering correlation.
In this situation, the product of multiplier of all PSFs is N. And the conditional expectation when turns to is like this.
Substituting these expressions, we can obtain multiplier of stress considering correlation.
The correlation between 2 or more PSFs. The influence of all PSFs are strong, and HEP increases N times. PSF[S] refers Stress, and PSF[A]~[G] refer the other PSFs.
We consider a situation where all 8 PSFs influence on HEP, and HEP increases N times. And finally, calculate 𝑥_𝑆’ which is multiplier of stress considering correlation.
In this situation, the product of multiplier of all PSFs is N. And the conditional expectation when 𝑥_𝑠 turns to 𝑥_𝑠′ is like this.
Substituting these expressions, we can obtain multiplier of stress considering correlation.