## Slide 1: Evaluation of PSA Methods for Non-Light Water SMRs
Presented by: Wes Brinsfield - Jensen Hughes
Co-Authors:
Yochan Kim and Dr. Jinkyun Park - Korea Atomic Energy Research Institute (KAERI)
Dr. Seong Kyu Park – Nuclear Engineering Services and Solutions (NESS)
Dr. Young Wook Chung – FNC Technology Co., LTD
Jeffrey Julius – Jensen Hughes
Eric Thornsbury – EPRI (Project Manager)
PSAM 18 – Pittsburgh, Pennsylvania, USA
Session 1-3: SMR and Advanced Reactor Risk Assessment and Licensing – I (Abstract WB210) July 20, 2026

## Slide 2: Overview of EPRI Research Project

## Slide 3: Overview of EPRI Research Project
Overview of project
  Task 1: Evaluation of applicability of current generation PSA Methods to non-Light Water (NLW) – Small Modular Reactor (SMR) Designs – THIS PRESENTATION
      For issues similar to those for existing plant designs
      For issues unique for NLW-SMR designs
      Focus on high temperature gas reactor (HTGR) and molten salt reactor (MSR) but not limited to these designs
  Task 2: PSA Methodology for Flexible Operation of the NLW-SMR
    Evaluate impact on PSA for designs with the capability to perform flexible operations (i.e., beyond baseload)
      Companion report in draft now (expected publication late 2026)

## Slide 4: Reports, Task 1
Evaluation of Probabilistic Safety Assessment Methods for Non-Light Water Small Modular Reactors (HTGR and MSR), EPRI, Palo Alto, CA: 2026. 3002034425. KAERI/RR-5394/2025.
  PUBLICLY AVAILABLE – FREE DOWNLOAD FROM EPRI.COM

## Slide 5: Overview of Task 1 Approach
Notes: Sections 1 & 2: Objectives, Scope, Completeness, Assumptions, Approach

## Slide 6: Overview of Task 1 Approach
Scope:
  “Fueled operation” - risk of radionuclide release after initial fuel load, through plant operations until such time that the reactor is permanently shut down for decommissioning
  Does not include the use of nuclear power for propulsion and remote power applications (maritime (ships), aviation (airplanes), spacecraft (satellites, rockets)
Completeness (PSA considerations) based on:
  ASME/ANS RA-S-1.1–2022, PRA Standard, 2022
  ANS/ASME-58.22-2014, Low Power and Shutdown PRA [Standard for Trial Use], 2017
  ASME/ANS RA-S-1.4-2021, PRA Standard, Advanced NLW Nuclear Power Plants (NPPs), 2021
  IAEA SSG-3 (Rev-1), Level 1 PSA for NPPs, 2024
  IAEA-TECDOC-2003, Lessons Learned in Regulating SMRs, 2022
  OECD/NEA, CSNI Technical Opinion Paper No. 21: Research Recommendations to Support the Safe Deployment of SMRs, 2023

## Slide 7: Overview of Task 1 Approach (continued)
Task 1 topic areas for assessment (these are known as “Current Assessment Concentrates” (CACs)):
CAC Number | CAC
1 | Initiating event (IE) identification and quantification
2 | Data
3 | Human reliability analysis (HRA)
4 | Success criteria
5 | Source term and radiological consequences
6 | Internal fire, seismic, and additional external hazards (natural and related to human activities (e.g., nearby industrial facility))
7 | Safety goals
8 | Plant operating state (POS)

## Slide 8: Overview of Task 1 Approach (continued)
Each CAC assessed against a set of Considerations and Sub-considerations with the objective to determine if existing PSA methods could be used to address the CAC within the context of those considerations and sub-considerations
  Identify gaps in methodology
  Recommend actions to close/eliminate the gaps

## Slide 9: Overview of Task 1 Approach (continued)
Consideration Number | Consideration for NLW-SMRs | Sub-Considerations
1 | Risk metrics | General risk definition Fuel safety
2 | Novel Features of NLW-SMRs Unique design features Multiple units with potential dependencies Operating temperature and pressure | Passive systems Operating Temperature and Pressure (T and P) Multiple modules Shared systems Shared/reduced (human) resources Operation support systems with high level of automation
3 | Mode of operation | Power operation Low power Hot standby Hot shutdown Cold shutdown Refuelling Off-normal operation
4 | Industrial applications | Electricity generation (load following) Electricity generation (base load) Hydrogen generation Heat generation Desalinization Others (if necessary)
5 | Flexible siting | On ground Underground Floating Underwater Movable In regions lacking essential infrastructure (e.g. electrical grid, cooling water) Module transportation during operation of other modules Module transportation for refuelling purposes
6 | Regulatory considerations | 

## Slide 10: Example Of CAC Assessment
Notes: Sections 1 & 2: Objectives, Scope, Completeness, Assumptions, Approach

## Slide 11: Example of CAC Assessment
Consideration | Sub-Considerations | Potential or Actual Gap | Suggestions for Resolution
Initiating Events (CAC 1) – Level 1 PSA |  |  | 
1. Risk metrics | 1.1 General risk definition | Undeveloped criteria for screening IEs from additional consideration, e.g., low frequency, low conditional probability of release given IE or very low frequency (but subject to uncertainty) with a high conditional probability of release Criteria for screening of IE to address multiple or consequential initiating events such as SBO, ATWS, and seismic-tsunami. Impact of multiple hazards on NLW-SMRs (e.g., seismically induced fires). Initiating events leading directly to release (e.g., Level 2) are discussed immediately following this table (Level 2 IE). | Sensitivity analyses using PSA models Align initiating events with Licensing Basis Events (LBEs) in Frequency-Consequence curve of NEI 18-04 (Ref. 21). Expand MLD / FMEA to include multiple hazards that are consequential or related empirically (ensure screening criteria includes and addresses likelihood of such events).
 | 1.2 Fuel safety of NLW-SMRs that utilize novel fuel designs (Note 1) | Unclear impacts of accident-tolerant fuel on risk (e.g., reduced frequency of release). | Continue laboratory and in-field testing. Deterministic analyses.
2. Design Unique design features Multiple units with potential dependencies Operating temperature and pressure | 2.1 Passive systems (other sub-considerations not shown) | None because passive system failures either would not cause an IE or would map to an existing IE group. | 
Assessment of gaps – initiating event CAC (CAC 1) (only first two Considerations shown; only CAC 1 (out of 8) shown)

## Slide 12: Results: Applicability of PSA Methods
Notes: Sections 1 & 2: Objectives, Scope, Completeness, Assumptions, Approach

## Slide 13: Applicability of PSA Methods for NLW-SMR Designs
PSA aspect |  | Applicability of PSA methods to NLW-SMRs | Potential Gaps
CAC 1- IE identification and quantification |  | High | Combined hazards, LPSD IEs
CAC 2 - Reliability data |  | High | Defining HW/SW interfaces and component boundaries for digital components
CAC 3 - Human reliability analysis |  | Medium | Additional failure modes or failure mechanisms; additional recovery; LPSD modes of operation
CAC 4 - Success criteria analysis |  | High | Definition of “success”
CAC 5 - Source term calculation, off-site radiological consequences |  | High | Lack of efficiently running realistic source term codes. (MELCOR and other codes are evolving to include new models)
CAC 6 – | Fire IE frequencies and PSA modeling | Medium | Fire IE frequencies Fire modeling (e.g., Digital systems (such as fiber optic cable)) Scenarios involving sodium or other reactive coolants LPSD Fire PSA modeling guidance
 | Seismic IE frequencies and fragility analyses | High | 
 | Screening of hazards | High | Industrial applications
CAC 7 - Safety goals |  | Low | Risk metrics and end states for NLW-SMR designs
CAC 8 - Evaluation of plant operational states |  | Medium | Online refueling, different operating ,lack of OPEX.
Specific Considerations/Sub-Considerations and Other Topics |  |  | 
Reliability of passive systems |  | Medium | Use of advanced/inherent passive features
Digital I&C modeling |  | Medium | Applicability of current HRA methods for DI&C
Multi-unit PSA |  | Medium | Applicability of current methods for multi-unit SMR plants
NEI 18-04 |  | Medium | No integrated quantification tool to propagate risk results and impacts of uncertainties
Automation Reliability |  | Medium | See CAC 3 – HRA

## Slide 14: High Level Conclusions
Current PSA methods as developed for several elements of LWR PSAs are generally applicable
However, gaps may exist (see previous table)
  LPSD and other Plant Operating States
  Fire PSA
  Integrated risk quantification
  Data collection and analysis
  Source term modeling and quantification
  Safety goal definition

## Slide 15: Opportunities for Future Research
Notes: Sections 1 & 2: Objectives, Scope, Completeness, Assumptions, Approach

## Slide 16: Future Research Candidates
Case studies –
  E.g., hypothetical/prototype HTGR or MSR design
    defining risk metrics, identifying source terms and release categories, establishing initiating events appropriate for the design, etc.
  LPSD Fire PSAs
Integrated risk quantification
  Produce frequency/consequence results of NEI 18-04 approach
    A mechanism to automate quantification that allows the user to define acceptance criteria and to “flag” (highlight) sequences
    A technique to easily group families of sequences and link those groupings to an uncertainty code

## Slide 17: Future Research Candidates (continued)
Formalized expert judgement process
  When and how to develop and qualify expert judgement
Safety goals
  More general and applicable PSA end states and risk metrics should be considered and developed for HTGR and MSR NPPs