## Slide 1: Human Reliability Analysis for Human-Induced Common-Cause Failures
2026.07.22
○Yuta Yanada, Kanoko Nishiono, Tingting Cheng, Ali Mosleh
The contents of this document represent the opinions of the authors and do not represent the opinions of the Nuclear Regulation Authority.
Probabilistic Safety Assessment and Management PSAM 18,
July 19-July 24, 2026, Pittsburgh, Pennsylvania

## Slide 2: Table of Contents
Background and Objective
Methodology
Analytical Conditions
Result
Conclusion

## Slide 3: Background and Objective
Human-induced Common Cause Failures (CCFs) can significantly degrade plant reliability.
It is needed to model the causal relationship between Human Failure Events (HFEs) and common causes in HRA.
maintenance, inspection
Scope of HRA
Initiating Event
Eq1
Eq2
Eq3
Human Failure Event (HFE)1
HFE2
Root Cause
procedure, skill, training, work plan, safety culture, design
common cause
Scope of PRA
Human-induced CCF
Proceed next HFE
In this study, we proposed a method to consider causal relationship.
Using proposed method, evaluate the human-induced initiating events.

## Slide 4: Adopted Phoenix HRA modeling framework
IE
Critical Task 1
Success
Failure
CF 1
IE
Critical Task 2
Success
Failure
CF 2
Critical Task 1
Information
Decision
Action
Crew Failure Mode
(CFM) 1
CFM 2
…
…
Performance Influencing Factor (PIF) 1
PIF 2
PIF 3
Critical Task 2
I
D
A
CFM 3
CFM 4
…
…
PIF 3
PIF 4
Bayesian Belief Network (BBN)
Without dependency
When the dependency is not considered, each PIFs is independent
independent
independent

## Slide 5: Methodology for considering common cause
By treating the common causes of HFEs as performance influencing factors (PIFs) and applying the dependency analysis method of Phoenix, an HRA was conducted that accounts for the common causes underlying human-induced CCFs.
Critical Task 1
Information
Decision
Action
Crew Failure Mode
(CFM) 1
CFM 2
…
…
PIF 1
PIF 2
PIF 3
Critical Task 2
I
D
A
CFM 3
CFM 4
…
…
PIF 3
PIF 4
Bayesian Belief Network (BBN)
Dependency methodology of Phoenix
PIF 3
Common Cause
IE
Critical Task 1
Success
Failure
CF 1
IE
Critical Task 2
Success
Failure
CF 2

## Slide 6: Analytical scenario for trial calculation
This scenario is based on an actual incident that occurred in a nuclear power plant in Japan.
At unit 1, an inspection of step-up transformer protection relay was occurred. While unit 2 was at the rated power.
This task includes isolation operation of the current transformer (CT) circuits at the step-up transformer protection relay panel.
The task was configured in operations for two train (Unit1 A and Unit1 B).
After the operation for Unit1 A was performed, the operation for Unit1 B was performed.
Reactor trip
 | Instructor | Executor
Unit1 A operation (step1~step7) | Highly experienced crew | Unexperienced crew
Unit1 B operation (step8~step14) | Unexperienced crew | Highly experienced crew

## Slide 7: Overview of analytical model for trial calculation
Unit1A maintenance
Unit1B maintenance

## Slide 8: Branching of each selection and operation
Critical Task 1
Critical Task 2
CF 2,4,6,8,10,12,14,16
CF 3,5,7,9,11,13,15,17

## Slide 9: Example for Determination of PIFs related to each CFMs
Critical Task 2
Critical Task 1
Critical Task 2
I
D
A
Incorrect operation of component
Critical Task 1
Information
Decision
Action
Action on wrong component
Human System Interface
Task Load
PIF
CFM
CFM
PIF
The unit identification marking is positioned outside the operator’s field of view during work.
Task load for continuation of repetitive tasks and
the large number of procedural steps

## Slide 10: Without dependencies as common causes of different HFEs
A
A
Human System Interface
Procedure
Human System Interface
Procedure
・・・
Knowledge and Abilities-Crew A
Team Effectiveness
Knowledge and Abilities-Crew A
Team Effectiveness

## Slide 11: With dependencies as common causes of different HFEs
Using BBN, the dependency is considered

## Slide 12: Quantification Process
The occurrence probability of a CFM is assigned to each combination of degraded and non-degraded PIF states.
Since Phoenix HRA defines eight primary PIFs, the table contains 28=256 possible combinations of PIF states.
Human System Interface (HSI) | Degradation (D) |  |  |  | Nominal (N) |  |  | 
Procedure | D |  | N |  | D |  | N | 
Knowledge and Abilities | D | N | D | N | D | N | D | N
Probability of action on wrong component | 0.001995 | 0.001390 | 0.001459 | 0.000853 | 0.001228 | 0.000622 | 0.000691 | 0.000085
Example for conditional probabilities table (CPT) of CFM, “action on wrong component”
The degradation probability of a PIF is obtained by the PIF values implemented in the Phoenix tool.
When dependencies are taken into account, the degradation probability is updated using a Bayesian Belief Network (BBN).

## Slide 13: Example for quantification of CF4 “selection of trip terminal for unit1 A”
HSI | Degradation (D) |  |  |  | Nominal (N) |  |  | 
Procedure | D |  | N |  | D |  | N | 
Knowledge and Abilities | D | N | D | N | D | N | D | N
Probability of action on wrong component | 0.001995 | 0.001390 | 0.001459 | 0.000853 | 0.001228 | 0.000622 | 0.000691 | 0.000085
Without dependency
P(CF4) = P(DDD)+P(DDN)+P(DND)+P(DNN)+P(NDD)+P(NDN)+P(NND)+P(NNN)
0.001125
 | HSI | Procedure | Knowledge and Abilities
Degradation probability | 0.667 | 0.7 | 0.25
Example for CPT table of CFM, “action on wrong component”
PIF degradation probability
When dependency is considered, HSI and Procedure degradation probability is updated due to success for CF2 and Knowledge and Abilities degradation probability is updated due to success for CF3.

## Slide 14: Comparison of results with and without dependency consideration
Considering common cause of multiple HFEs slightly reduced the End-State HEP compared with the case without considering of common cause.
→The scenario proceeds to the next CF only when the preceding CF is successful, and no subsequent CF remains once any CF fails. Therefore, the dependency effect is limited to the impact of preceding CF success.
When common cause of HFEs are considered, HEP does not change for CF2–CF9, but decreases for CF10–CF17.
→Among the common cause PIF, “Knowledge and Abilities - crew A” and “Team Effectiveness” are the main contributors. The other PIFs show no noticeable impact.

## Slide 15: Conclusion
In this study, HRA was conducted that accounts for common causes of multiple HFEs, and the probability of initiating events resulting from these HFEs was estimated.
As an approach to incorporating the relationship between common causes and HFEs, a method using the dependency analysis technique of Phoenix HRA was proposed.
A trial HRA analysis was conducted using Phoenix, focusing on an accident that occurred during past maintenance work.
The trial analysis showed that, when common causes of human-induced CCF are taken into account, the HEP of a task following the successful completion of a preceding task tends to decrease.
Additional trial analyses are required using human event scenarios that include recovery actions following the failure of a task.

## Slide 16: Appendix: Determination PIFs related to each CFMs (1)
PIF/PIF level | CFM | Critical Task | Relevant CFs | Description
Human System Interface (HSI) /0.667 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF2, CF4, CF6, CF8, CF10, CF12, CF14, CF16 | Because the unit identification markings on the panels were common across all panels, the CFs related to panel selection share a common PIFs.
Resource /0.333 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF16 | The layout structure was such that it was prone to inducing errors in panel selection in CF16.
Knowledge and Abilities for Crew A /0.25 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF1, CF10, CF11, CF12, CF13, CF14, CF15, CF16, CF17 | In the series of operations for the B train, a potential lack of attention by Crew A, attributable to their high level of task familiarity, was considered.
 | Incorrect Operation of component | The crew correctly performs the procedural step |  | 

## Slide 17: Appendix: Determination PIFs related to each CFMs (2)
PIF/PIF level | CFM | Critical Task | Relevant CFs | Description
Knowledge and Abilities for Crew B /0.25 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF2, CF3, CF4, CF5, CF6, CF7, CF8, CF9 | In the series of operations for the A train, insufficient task experience of Crew B was considered.
 | Incorrect Operation of component | The crew correctly performs the procedural step |  | 
Task Load /0.375 | Incorrect Operation of component | The crew correctly performs the procedural step | CF7, CF9, CF15, CF17 | Increased task load due to the continuation of repetitive tasks and the large number of procedural steps was considered.
Bias /0.333 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF16 | It was considered that an assumption existed that “performing the same actions as in the A‑train work would be sufficient.”

## Slide 18: Appendix: Determination PIFs related to each CFMs (3)
PIF/PIF level | CFM | Critical Task | Relevant CFs | Description
Team Effectiveness /0.214 (3/14) | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF1, CF10, CF11, CF12, CF13, CF14, CF15, CF16, CF17 | In the series of operations for the B train, the work was not sufficiently supervised due to an inappropriate team composition.
 | Incorrect Operation of component | The crew correctly performs the procedural step |  | 
Procedure /0.7 | Action on Wrong component | The crew correctly select the trip terminal for Unit1 | CF2, CF4, CF6, CF8, CF10, CF12, CF14, CF16 | When selecting the panel, the procedure did not include a step requiring confirmation of the target unit.

## Slide 19: Appendix: Critical Function of Master Event Sequence Diagram(ESD)

## Slide 20: Appendix: Analytical model for trial analysis
Critical Task 2
Critical Task 1
Critical Task 2
I
D
A
CFM 3
CFM 4
…
…
PIF 3
PIF 4
Critical Task 1
Information
Decision
Action
CFM 1
CFM 2
…
…
PIF 1
PIF 2
PIF 3
Without dependency
BBN

## Slide 21: Appendix: Analytical model for trial analysis
Critical Task 2
Critical Task 1
Critical Task 2
I
D
A
CFM 3
CFM 4
…
…
PIF 4
Critical Task 1
Information
Decision
Action
CFM 1
CFM 2
…
…
PIF 1
PIF 2
PIF 3
With dependency
BBN