## Slide 1
A Comparative Study of PRA Methodologies for Light-Water and Advanced Reactors
July 19 – July 24, 2026
Zhegang Ma, Ph.D., P.E.
Zhegang.Ma@inl.gov
INL/CON-26-93952
Hayden Spencera, Jisuk Kimb, Zhegang Mab, and Vaibhav Yadavb
a Oregon State University, Corvallis, Oregon, USA
b Idaho National Laboratory, Idaho Falls, Idaho, USA

## Slide 2: Background
Idaho National Laboratory (INL) is leading an ongoing project to develop and demonstrate a methodology that leverages multimodal large language models (LLMs) to generate computer programs for nuclear risk and reliability analysis
The outcome of this effort will provide safety analysis teams with a tool to automate the development of probabilistic risk assessment (PRA) models
Existing PRA guidance and documentation are primarily based on currently operating light-water reactors (LWRs)
As advanced reactors (ARs) introduce new technologies, safety functions, system designs, and licensing approaches, it is important to understand how PRA methodologies differ so that LLM-based tools can accurately interpret and generate PRA models for these reactor designs
To address this need, a comparative study of PRA methodologies for LWRs and ARs was conducted to assess the state of the art in risk and safety analysis for both reactor types

## Slide 3: Background (cont.)
Five representative LWRs and eight ARs were selected to examine differences in risk assessment scope, methodologies, and modeling practices
The comparison focused on
  Initiating events
  Event trees
  Fault trees
  Data analysis
  Human reliability analysis
  End states
  Assumptions (such as mission time)

## Slide 4: Background (cont.)
Primary source materials include publicly available
  PRA reports
  Safety analysis reports
  Licensing application documentation
  Topic reports
  White papers
This presentation summarizes the major observations and insights from these comparative efforts
The findings are expected to enhance the performance and applicability of LLM-based tools for nuclear risk and safety analysis

## Slide 5: Selected LWRs and ARs
LWR
Surry Power Station
AR
NuScale Small Modular Reactors (SMR)
Sequoyah Nuclear Plant
Advanced Power Reactor 1400 (APR1400)
Peach Bottom Atomic Power Station
Grand Gulf Nuclear Station
Standard Modular High Temperature Gas-Cooled Reactor (MHTGR)
Kemmerer Power Station’s Natrium reactor
Hermes
Xe-100
Oklo Aurora Powerhouse
Kaleidos
Integral Molten Salt Reactor (IMSR)
Notes: NuScale US600 SMR: small modular PWR with up to 12 modules. Each module can provide 160 MWth (50MWe). It has natural circulation for the reactor coolant system (RCS), so it does not need coolant pumps. It uses UO2 with less than 4.95% enrichment and is refueled every 24 months.
Standard Modular HTGR: The MHTGR is cooled by helium as its primary and secondary coolant with circulators. It uses uranium oxycarbide (UCO) as fissile material and THO2 as fertile material with an average U-235 enrichment of 19.9%. The fuel is coated with a tri structural isotropic (TRISO) coating.
The Natrium: The Natrium is a pool-type sodium fast reactor with metallic uranium-zirconium high-assay low-enriched uranium fuel (HALEU). Sodium is in both the primary and intermediate heat transport systems supplied by sodium pumps.
Hermes: The Hermes reactor will be a fluoride salt cooled high temperature reactor. It will be fueled by TRISO fuel particles and HALEU. There is no secondary coolant in the Hermes reactor. Hermes is a test reactor which will not produce electricity.
Xe-100: a pebble bed HTGR. It can be up to four reactors together for about 320MWe generated. It is fueled by TRISO coated UCO, the U-25 enrichment is 15.5%. The primary coolant is helium.
Aurora: a liquid metal cooled reactor. It is a metal- fueled fast reactor.
Kaleidos: a HTGR microreactor that can have modules combined for any output of energy. The primary coolant is helium, and it uses circulators to circulate the helium. It uses TRISO fuel which needs to be refueled every 5 years
Integral Molten Salt Reactor: The IMSR uses low enriched uranium (less than 5%) in a liquid form in uranium tetrafluoride and dissolved in a mixture of salt. This mixture is a nuclear fuel, coolant and a heat transfer medium. In the secondary coolant there is a non-radioactive salt that can remove the heat from the fuel salt

## Slide 6: Initiating Events
LWRs and ARs have many initiating events in common such as general transients, Loss of Offsite Power (LOOP), Loss of Coolant Accident (LOCA), while ARs could have new ones that are specific to the reactor design
ARs could have new initiating events that are specific to the reactor design
  Modular design: module-specific initiating events
  Unique systems such as helium, heat transport system (HTS), pebble, and molten salt:
    MHTGR: loss of main cooling, HTS different secondary system.
    Xe-100: helium pressure boundary leaks or breaches
    Hermes: salt spills, pebble-handling malfunctions
    Kaleidos: primary loop depressurization (leaks from hot leg, cold leg, heat exchanger, or pressure vessel)

## Slide 7: End States
Typical end states for LWR and AR PRAs include safe shutdown (OK), core damage (CD), and release categories
  NuScale: success state(OK), core damage (CD), no release (NR), or large release (LR)
  MHTGR: characterizes the end states in terms of release categories
Xe-100: defines the end state according to licensing basis event (LBE) categories including anticipated operational occurrence (AOO), design basis event (DBE), and beyond DBA (BDBA)
Natrium: either safe, stable plant condition or radionuclides release
Hermes: evaluates dose consequences using the Maximum Hypothetical Accident (MHA)

## Slide 8: Event Trees and Fault Trees
LWRs and ARs have a few common mitigating systems, while ARs introduce a variety of novel systems different from the LWRs, as the reliance on passive system represents one of the major differences
New systems and safety functions in ARs require reactor-specific PRA models rather than simple extension of existing LWR models
NuScale: (1) passive emergency core cooling system (ECCS); (2) passive decay heat removal system (DHRS)
Natrium: (1) reactor air cooling (RAC) system relying on natural convection for decay heat removal; (2) intermediate air-cooling system with a passive circulation mode; salt-based systems and heat transport systems, such as nuclear island salt system (NSS), the energy island salt heat transport system (ESS), the thermal salt storage system (TSS)

## Slide 9: Event Trees and Fault Trees (cont.)
Hermes: (1) passive DHRS; (2) tritium management system to capture the tritium from gas streams to reduce the release; (3) primary heat transport control system that controls the transport of the primary coolant and maintains it in a liquid state; (4) heat rejection subsystem that is a part of the primary heat transport system and transports heat from the coolant to the atmosphere
Xe-100: (1) reactor cavity cooling system (RCCS) that passively removes the decay heat; (2) fully passive internal reactor vessel auxiliary cooling system (IRVACS)
MHTGR: (1) helium purification subsystem that removes the chemical impurities from the helium to maintain concentration of primary coolant; (2) helium storage and transport subsystem with high-pressure storage tanks that can provide makeup and purge helium, and low-pressure storage tanks that receive helium.

## Slide 10: Data Analysis
LWRs use generic industry data and plant-specific data for initiating event frequencies, component failure rates, and common cause failure probabilities in their PRA
ARs would similarly rely on generic data because plant-specific operating experience is limited
  Adjustments to the generic data may be needed to better reflect the plant design characteristics
Some ARs are exploring simulation-based approaches to generate representative operational information
  Xe-100 employs digital twin to produce simulated operating data
  Kaleidos developed a software platform, SimEngine, to build digital twins and model reactor performance under a variety of conditions

## Slide 11: Human Reliability Analysis
Both LWR and AR HRAs consider pre-accident and post-accident errors, using HRA methods such as accident sequence evaluation program (ASEP), Technique for Human Error Rate Prediction (THERP), and SPAR-H
ARs could rely on technology and passive designs to reduce or eliminate operator errors
MHTGR adopts a distinct approach, with an operator response model that emphasizes cognitive errors rather than procedural ones, reflecting its reliance on computer-controlled and passive safety system
No operator actions are required in Xe-100 to maintain fuel temperature within safe limits -> the integrated modular automatic control (IMAC) system verifies operational parameters before allowing progression to subsequent steps

## Slide 12: Mission Time
LWR PRAs generally assume a 24-hour mission time
Most ARs specify longer timeframes, e.g.,
  The Natrium reactor adopts a 72-hour mission time for the bottled air injection system
  NuScale SMR applies a 72 hours beginning at the onset of the initiating event, requiring systems and components to remain functional throughout this period

## Slide 13: Comparison Table
Topic | LWR | Advanced Reactors
Initiating Events | Classic PRA initiating events | Design-specific events
End State | Core damage, large release | Core damage, release category, dose consequence
Safety Systems | Mostly active mitigating systems | Increased passive systems
Data | Industry + plant | Generic + simulation
HRA | Existing methods | Automation reduces operator actions
Mission Time | 24 h | Longer, such as 72 h

## Slide 14: Summary
This research reviews and compares PRA methodologies for LWRs and ARs
The overall PRA framework remains largely consistent between LWRs and ARs, while differences arise primarily from reactor technologies, safety philosophies, and licensing approaches
The greatest limitation of this study is the limited availability of publicly accessible information for many advanced reactor designs
This study should be updated as additional PRA and licensing information for advanced reactors becomes publicly available
Notes: Only two of the selected ARs have publicly available PRAs (NuScale SMR and MHTGR), and two others (Natrium and Xe-100) have Preliminary Safety Analysis Reports

## Slide 15: Acknowledgement
This work of authorship was prepared as an account of work sponsored by Idaho National Laboratory (under Contract DE-AC07-05ID14517), an agency of the U.S. Government. Neither the U.S. Government, nor any agency thereof, nor any of their employees makes any warranty, express or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights.
This work was supported in part by the U.S. Department of Energy, Office of Science, Office of Workforce Development for Teachers and Scientists (WDTS) under the Science Undergraduate Laboratory Internships Program (SULI).

## Slide 16: References
[1] U.S. Nuclear Regulatory Commission. (1990). Severe Accident Risks: An Assessment for Five U.S. Nuclear Power Plants — Final Summary Report (NUREG-1150, Volume 1): Part 1, Part 2, Part 3.
[2] Virginia Electric and Power Company. (2018). Surry Power Station Updated Final Safety Analysis Report.
[3] Tennessee Valley Authority. (2020). Sequoyah Nuclear Plant Updated Final Safety Analysis Report
[4] A. M. Kolaczkowski, W. R. Cramond, T. T. Sype, K. J. Maloney, T. A. Wheeler, S. L Daniel. (1989). Analysis of Core Damage Frequency: Peach Bottom, Unit 2 Internal Events. Sandia National Laboratories.
[5] M. T. Drouin, J. L. LaChance, B. J. Shapiro, S. Miller, T. A. Wheeler. (1989). Analysis of Core Damage Frequency: Grand Gulf, Unit 1, Internal Events. Sandia National Laboratories.
[6] Entergy Operations, Inc. (2016). Grand Gulf Nuclear Generating Station Updated Final Safety Analysis Report Chapter 15 Accident Analyses.
[7] Korea Electric Power Corporation, Korea Hydro & Nuclear Power Co., LTD. (2018). APR1400 Design Control Document.
[8] NuScale Power, LLC. (2020). NuScale Standard Plant Design Certification Application, Chapter 19 Probabilistic Risk Assessment and Severe Accident Evaluation.
[9] X Energy, LLC. (2024). Xe-100 Licensing Topical Report Transient and Safety Analysis Methodology.
[10] D. Nigh. (2022). Xe-100 PRA Technical Adequacy Approach. X Energy LLC. U.S. Nuclear Regulatory Commission.
[11] E. J. Mulder. (2021). Overview of X-Energy’s 200 MWth Xe-100 Reactor. National Academy of Sciences.
[12] U.S Nuclear Regulatory Commission. (2025). Oklo Aurora Powerhouse. Oklo Aurora Powerhouse | NRC.gov
[13] TerraPower, LLC. (2024). Kemmerer Power Station Unit 1 Preliminary Safety Analysis Report.
[14] C. Yang. (2023). Regulatory Engagement Plan. Radiant Industries, Inc. https://www.nrc.gov/docs/ML2328/ML23286A328.pdf.
[15] J. B. Tompkins, B. Betzler, B. Urberger, D. Bernauer. Design and Demonstration of the Kaleidos Portable Nuclear Microreactor. National Organization of Test, Research and Training Reactors.
[16] Terrestrial Energy USA, Inc. (2022). IMSR Core-unit Definition – Applicable Structures, Systems and Components – Revision 1.
[17] GA Technologies Inc. (1987). Probabilistic Risk Assessment for the Standard Modular High Temperature Gas-Cooled Reactor.
[18] M. Hiser. (2023). Summary of February 9, 2022, Public Meeting on the Kairos Hermes Preliminary Safety Analysis Report. U.S. Nuclear Regulatory Commission.
[19] Kairos Power LLC. (2021). Hermes Non-Power Reactor Preliminary Safety Analysis Report, Revision 3.
[20] ASME/ANS. (2021, February). Probabilistic Risk Assessment Standard for Advanced Non-Light Water Reactor Nuclear Power Plants, ASME/ANS RA-S-1.4-2021.
[21] U.S. Nuclear Regulatory Commission. (2022). TRIAL - Acceptability of Probabilistic Risk Assessment Results for Non-Light Water Reactor Risk-Informed Activities.

## Slide 17: References
[22] U.S. Nuclear Regulatory Commission. (1983). PRA Procedures Guide: A Guide to the Performance of Probabilistic Risk Assessments for Nuclear Power Plants (NUREG/CR-2300, Volume 1 & 2).
[23] U.S. Nuclear Regulatory Commission. (2007). Industry-Average Performance for Components and Initiating Events at U.S. Commercial Nuclear Power Plants (NUREG/CR-6928).
[24] Z. Ma, T. E. Wierman, and K J. Kvarfordt. (2021). Industry-Average Performance for Components and Initiating Events at U.S. Commercial Nuclear Power Plants: 2020 Update (INL/EXT-21-65055).
[25] Z. Ma and K J. Kvarfordt. (2022). CCF Parameter Estimations, 2020 Update (INL/EXT-21-62940, Rev. 1).
[26] U.S. Nuclear Regulatory Commission. Standard Review Plan for the Review of Safety Analysis Reports for Nuclear Power Plants: LWR Edition (NUREG-0800, Formerly issued as NUREG-75/087).